## Slide 1: Lean Six Sigma Certification & Training
Module 010 Section 002
Process Mapping

## Slide 2
Learning Objectives
Learn how Process Mapping fits in with Process Improvement
Overview the uses of a Process Map
Learn how to build a Process Map, step by step
Difference between Top Level Map & a Detail Map
Complete a Process Mapping Exercise
Review examples of Process Maps

## Slide 3
Process Mapping
Should Describe:
  Major activities/tasks
  Sub-processes
  Process Boundaries (top level vs. detail)
  Process Inputs X’s
  Process outputs Y’s
  Process step outputs y’s
Should be reviewed frequently and updated
Notes: Remember y is our output and variability is caused by variability in the various inputs x

## Slide 4: What Is A Process Map?
A graphical representation of a process flow identifying the steps of the process, the x’s and y’s of the process and opportunities for improvement.

## Slide 5: Process Maps are Hierarchical
Top Level Flow Map
  Major Use - to locate critical features or processes
  Usually focused on process sequence for a product
  It is characterized by a linear flow from one process step to the next
  Follows the process sequence, but usually lacks sufficient detail for a new person to successfully complete the task.
Detail Process Flow Map
  Major Use - to understand details of how a process works, decision points
  Usually focused on one or two processes in a work area
  It should be used for Work Instructions
  It is used to develop the FMEA and Control Plan
  It is characterized by convoluted decision paths
  Following the map should lead to successful completion of the task
There can be several levels of detailed maps.
Notes: An Assembly of a Part into an Engine?

## Slide 6: The Process Map Has Many Uses
1. Provides a step-by-step picture of the “as-is” situation for discussion and/or communication.
2. Defines and highlights areas for improvement in a process. These can either be elimination of non-value added steps or addition of needed steps depending on the desired outcome of the process.
3. Documents “hidden factory”.
Process maps can be used on any type of process: manufacturing, design, service, or administrative.

## Slide 7: Remember, The First Step In Creating A Process Map Is To Have A Well-Defined Problem Statement
Make sure management provides you with a well-defined problem statement.
You can help refine the problem statement using the 5 why’s, but management must ultimately define the issue.

## Slide 8
Body Assembly
INPUTS
OUTPUTS
(Big Y’s)
Assembly Labor
Procedures
Materials
Equipment, Fixtures
Environment
Cleanliness
Rework
Part to Print
Performance to Spec
Visually acceptable
Leak free
Identified
Clean
Packaged for use
Consistent standard
Step 1: Develop an Upper Level Process Map
Identify The Major Inputs and Customer Outputs for the Suspect Process
and Identify Possible Connections
Notes: This big picture Process map identifies the major inputs and customer required
outputs.
Customers may be external or next in line internal customers
The following slides will show more detail

## Slide 9
Step 2: Identify Process Steps Within Boundaries
Label Body
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Station 1 Body Assembly
Paperwork
1
Test
6
7
Stores
Why is one of the steps a diamond?
Notes: This is an approximation of the AD-Sp Dryer Body Assembly process
Operations 1 and 6 are identified as “Non-Value Added” tasks

## Slide 10: Map Inspection Points - Summary
Signalled by a decision diamond
Decision diamonds must pose a question -- no exceptions -- remains consistent with Mapping Alternative Paths.
An inspection point creates a pass or fail decision based on objective standards
Inspections may lead to a reversal of process flow direction, rework loop or a scrap.
Specific, objective questions are almost always better.
6
Test
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?

## Slide 11
Step 3: List Output Variables (little y’s) for Each Step (Process and Product)
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Body Assembly
Paperwork
1
7
Route Ticket
Orientation
Label adhesion
Greased O ring
Screw position adj.
Flush w/ surface
Label Body
O ring position
Cover orientation
Snap ring inserted
Stores
Functional
Assembly
Rework
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?
How do little y’s relate to big Y’s? What if they don’t?
Test
6
Notes: This slide identifies the significant process outputs

## Slide 12
Step 4: List inputs (x’s) for each process step
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Body Assembly
Paperwork
1
7
Route Ticket
Orientation
Label adhesion
Greased O ring
Screw position adj.
Flush w/ surface
Label Body
O ring position
Cover orientation
Snap ring inserted
Stores
Functional
Assembly
Rework
Bills of materials
ISO Procedures
Cleanliness
Material
Press Force
Material
Assy Technique
Amount of Grease
Material
Assy technique
Adjustment Pos.
Snap Ring
Insertion
Material
Test Capability
Calibration
Test
6
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?
How do the x’s relate to big Y’s and small y’s?

## Slide 13
Step 5: Characterize the Inputs as Noise, SOP, Controllable and Critical Inputs
X Critical
N Noise
S SOP
C Controllable
S Bills of materials
S ISO Procedures
S Cleanliness
C Material
X Press Force
C Material
S Assy Technique
C Amount of Grease
C Material
S Assy technique
N Adjustment Pos.
C Snap Ring
C Insertion
C Material
X Test Capability
S Calibration
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Body Assembly
Paperwork
1
7
Route Ticket
Orientation
Label adhesion
Greased O ring
Screw position adj.
Flush w/ surface
Label Body
O ring position
Cover orientation
Snap ring inserted
Stores
Functional
Assembly
Rework
Test
6
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?
Notes: Note the controllable parameters on the process map

## Slide 14
Process Input Variables
Noise Inputs (N): Input variables (X’s) that impact the output variables (Y’s) but are difficult, impossible or we choose not to control. Example: Environmental variables such as humidity, temperature
Standard Operating Procedures (SOP): A standard procedure for running the process.
Controllable Inputs (C): X’s that can be changed to see the effect on Y’s. Sometimes called “Knob” Variables
Critical Inputs (X): X’s that have been statistically shown to have a major impact on the variability of the Y’s.

## Slide 15
Step 6: Add the operating specifications and process targets for the Controllable and Critical Inputs (if available)
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Paperwork
1
7
Route Ticket
Orientation
Label adhesion
Greased O ring
Screw position adj.
Flush w/ surface
Label Body
O ring position
Cover orientation
Snap ring inserted
Stores
Functional
Assembly
Rework
Body Assembly
Test
6
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?
X Critical
N Noise
S SOP
C Controllable
S Bills of materials
S ISO Procedures
S Cleanliness
C Material
X Press Force
C Material
S Assy Technique
C Amount of Grease
C Material
S Assy technique
N Adjustment Pos.
C Snap Ring
C Insertion
C Material
X Test Capability
S Calibration
Notes: Note the controllable parameters on the process map

## Slide 16
Step 7: Identify steps as value added or non-value added
Value Added
Non-Value
Added
Body Assembly
Label Body
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Paperwork
1
1
Functional
Assembly
Rework
Route Ticket
Orientation
Label adhesion
Greased O ring
Screw position adj.
Flush w/ surface
O ring position
Cover orientation
Snap ring inserted
Test
6
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?
X Critical
N Noise
S SOP
C Controllable
S Bills of materials
S ISO Procedures
S Cleanliness
C Material
X Press Force
C Material
S Assy Technique
C Amount of Grease
C Material
S Assy technique
N Adjustment Pos.
C Snap Ring
C Insertion
C Material
X Test Capability
S Calibration
Notes: Note the controllable parameters on the process map

## Slide 17
The Big Picture
Process Map
Cause and Effects Matrix
FMEA
Initial Assessment of Capabilities and Control Plans
OUTPUTS
INPUTS
Functional
Assembly
Rework
Label Body
2
Insert Spirol
Pin
3
Assemble
Pistons
4
Assemble
Cover
5
Paperwork
1
1
Functional
Assembly
Rework
Route Ticket
Orientation
Label adhesion
Greased O ring
Screw position adj.
Flush w/ surface
O ring position
Cover orientation
Snap ring inserted
Test
6
Is the pin seated correctly?
Does the O ring function properly?
Is the cover aligned correctly?
S Bills of materials
S ISO Procedures
S Cleanliness
C Material
X Press Force
C Material
S Assy Technique
C Amount of Grease
C Material
S Assy technique
N Adjustment Pos.
C Snap Ring
C Insertion
C Material
X Test Capability
S Calibration

## Slide 18
Process Mapping Helpful Hints
Always Process map with a team. Rarely, does one person have all process knowledge.
Interrogate the process by watching in many different conditions.
You must watch the process as it happens to see the detail you need.
Don’t let space be an issue. Consider using post-its, as the process steps and post on a wall to get your initial ideas across.
If your map does not have enough space to list all the information, use numbered reference sheets as attachments.
Maintain your Process Maps with dates and update them as necessary. Use them as a reference.

## Slide 19
Summary
Learn how Process Mapping fits in with Process Improvement
Overview the uses of a Process Map
Learn how to build a Process Map, step by step
Difference between Top Level Map & a Detail Map
Complete a Process Mapping Exercise
Review examples of Process Maps
Importance of team and team member background

## Slide 20
References
Visio Software
Business Process Improvement, Harrington, H. James,
McGraw Hill, Inc. 1991. ISBN # 0-07-026768-5

## Slide 21
www.BeyondLean.com
Thank You!