## Slide 1: Lean Six Sigma Certification & Training
Module 001 Section 003
Analyse

## Slide 2: Analyse Overview
The goal of the Analyse phase is to identify and verify bottle necks, waste and complexity on the process
This Phase combines process tools with statistical analysis to focus in on root causes form the basis for solutions in the next phase of the project
Although this phase does emphasise statistics, in reality (again for service processes), due to the large amount of natural variation, descriptive statistics are often more relevant!!!
Notes: <number>

## Slide 3: Analyse Checklist
To complete the analyse phase ensure:
  Examined our processes and identified potential bottlenecks, disconnects and redundancies that could contribute to the problem on which we are focusing
  Conducted a value and cycle time analysis, locating areas where time and resources are devoted to tasks not critical to the customer IF appropriate (i.e. for cycle time / lean projects)
  Analysed data about the process and its performance to help stratify the problem, understand reason for variation in the process, and identify potential root causes
  Developed root cause hypothesis to explain the problem we are solving
  Investigated and verified our root cause hypothesis, so that we are confident we have uncovered one or more ‘vital few’ root causes that create our problem
Notes: <number>

## Slide 4: Analyse Steps
Step 7:
Baseline Process Performance (Y)
Step 8:
Identify Significant Variables (xs)
Step 9:
Explore Root Causes of Significant Variables (xs)
Toll Gate Review
Notes: <number>

## Slide 5: Step 7: Baseline Process Performance (Y)
The first step is all about baselining the project Y
The baseline helps:
  Gives a factual assessment of the extent of the problem
  Allows comparison between the performance of the current state, and the future process after solutions have been implemented
  Ys tend to be the sort of metrics that are sought after for benchmarking comparisons
  Depending upon the particular measure, the process capability and stability can be estimated for control purposes
Notes: <number>

## Slide 6: Step 7: Key Outputs
In completing step 7, you should produce at least the following:
  A measure of location for your critical Ys
  If appropriate, a measure for the variation around the Ys
  An analyse of the distribution of the Y data, and an estimate of how capable the measure is of meeting the customer’s specifications
  If possible a historical trace of your key measures to show variation and stability over time
Notes: <number>

## Slide 7: Step 7: Possible Tools
A few tools are applicable to this step:
  Location Measures
  Variation Measures
  Estimations of Population Parameters
  Process Capability Measures
  Statistical Process Control
Notes: <number>

## Slide 8: Step 7: Measurers of Location
Location refers to an estimate of the ‘typical’ value.
Common measures include:
  Mean
  Median
  Mode
  Geometric Mean
  Harmonic Mean
  Weighted Means*
What is an average then? Well, it depends on who you talk to, but two definition are that it can mean all of the above OR it just refers to the mean
Notes: <number>

## Slide 9: Step 7: MMM…
n
 x
x =
Mean (average):
Median (the middle value of an ordered list):
Mode (the most frequent value):
Median =
l + i
( )
n / 2 - F
f
l is the lower boundary of the median group
i is the width of the median group
F is the cumulative frequency up to the median group
f is the frequency in the median group
n
 f x
x =
f is the frequency
Tabulated Data
Mode=
l +
fm- fm-1
2fm- fm-1- fm+1
x i
l is the lower boundary of the modal group
Fm is the (scaled) frequency of the modal group
Fm-1 is the (scaled) frequency of the pre-modal group
Fm+1 is the (scaled) frequency of the post-modal group
Notes: <number>

## Slide 10: Step 7: MMM … an Exercise
Calculate the Mean, Median and Mode for the following data set:
Expenses | Mid Point (X) | Number of Receipts (f) | fX | CUSUM (F)
Under £5 | 2.50 | 2 | 5 | 2
£5 but under £10 | 7.50 | 6 | 45 | 8
£10 but under £15 | 12.50 | 8 | 100 | 16
£15 but under £20 | 17.50 | 12 | 210 | 28
£20 but under £30 | 25.00 | 10 | 250 | 38
£30 but under £40 | 35.00 | 4 | 140 | 42
£40 or more* | 45.00 | 2 | 90 | 44
 |  | 44 | 840 | 
Notes: <number>

## Slide 11: Step 7: MMM … Answers
Mean = 840/44 = £19.09
Median = 15 + ((44 / 2) –16) / 12) x £5 = £17.50
Mode = 15 + ((12 - 8) / 2 x 12 - 8 – 5*) x 5 = £16.82
Notes: <number>

## Slide 12: Step 7: Geometric, Harmonic Means
Geometric Mean: ‘the nth root of the product of n numbers’ used when averaging percentages:
E.g. 30% 20% 25% 31% 25%
  Arithmetic Mean = (30+20+25+31+25/5) = 26.2%
  Geometric Mean = (530x20x25x31x25) = 25.89%
Harmonic Mean: ‘the reciprocal of the arithmetic mean of the reciprocals of the data’ used for rates or ratio data:
E.g. 23g.m-1 25g.m-1 26g.m-1 29g.m-1 23g.m-1
  Arithmetic Mean = (23+25+26+29+23/5) = 25.013g.m-1
  Harmonic Mean = 1/((1/23+1/25+1/26+1/29+1/23)/5) = 25.89g.m-1
Notes: <number>

## Slide 13: Step 7: Relationship Between Mean, Mode and Median
Why do you feel poor when they quote the average income?!
Notes: <number>

## Slide 14: Step 7: Measures of Dispersion
Dispersion refers to the variability around the typical or average value.
Common measures include :
  Standard Deviation
  Range
  Quartile Ranges – Stability Factors
  Span
  Coefficient of Variation
  Coefficient of Skewness
  Index Numbers*
Notes: <number>

## Slide 15: Step 7: Standard Deviation Re-cap
.
(Xi – X)
(Xi – X)2
Σ (Xi – X)2
n
Σ (Xi – X)2
n
The distance between a point and the mean…
Convert it to an area because we don’t want –ves (we are going to add shortly)…
Σ (Xi – X)2
Obtain the total area…
Calculate the average…
Now get back to a distance measure …
Notes: <number>

## Slide 16: Step 7: Range, Quartiles, Process Stability
SF = Q1 / Q3
Process Measurement
Q3
Q1
Lowest Quarter
Of The Data
Highest Quarter
Of The Data
Process Measurement
Q3
Q1
Process Measurement
Q3
Q1
  Wide Curve
  Significant Variation
  Narrow Curve
  Minimal Variation
Q1
Q3
1
Q1
Q3
0
Quartile Values
Order Value =
l + i
O - F
f
( )
l is the lower boundary of corresponding group
i is the width of the group
F is the cumulative frequency up to the group
f is the frequency in the group

## Slide 17: Step 7: Calculating the Stability Factor
  Sample of transactions established the baseline cycle time
  Sort them into order, top down or bottom up
  Determine the median
  Determine QI and Q3 (Q1=n/4, Q3=3n/4)*
Cycle Time
(minutes)
SF = Q1/Q3
= 19/85
= 0.224
18
5
6
28
28
32
36
46
47
28
38
10
12
13
42
47
50
57
58
79
18
20
133
244
3920
82
88
97
98
100
Notes: <number>

## Slide 18: Step 7: Span
How long does the Customer expect the application to take?
Notes: <number>

## Slide 19: Step 7: Span, Seeing it From the Customer’s Point of View
Keeping it simple
Visually powerful
It measures & highlights what our customers see and feel by measuring our fulfilment process
Expressed in the units of the process we are measuring
Creates ‘line of sight’ with our associates so they can clearly understand what the customers feel
Notes: <number>

## Slide 20: Step 7: Span – Looking at the Difference Between the 5th & 95th Percentile
Notes: <number>

## Slide 21: Step 7: It Provides a Prompt to Tighten Our Performance By Reducing Variation
Notes: <number>

## Slide 22: Step 7: Other Measures of Dispersion
x
s x 100
Coefficient of variation =
s
3 (Mean-Median)
Coefficient of skewness =
Coefficient of Variation: s as a % of the arithmetic mean. The higher the %, the greater the variation
Coefficient of Skewness: relates to the shape of a histogram that could be drawn from the data results show positive, negative or zero skewness
Notes: <number>

## Slide 23: Step 7: Estimations of Population Parameters
It is unlikely that one is able to sample an entire population
However, we need to know the parameters (i.e. averages, measures of dispersion etc.) of the unknown but wider population, in order to make sound business decisions
Probabilities, and probability distributions can be estimated directly sample data e.g.:
  20 red forms , 30 blue forms in a sample, one could estimate that the chance of randomly selecting a red form was 40% =20/(20+30). Given 1000 forms, 400 ought to be red…
However, we can make statistical inferences about the population, based on samples using the appropriate Model probability distribution
Notes: <number>

## Slide 24: Step 7: The Usual Suspects…
The most common probability distributions for continuous data are the:
  Normal
  t
Three common probability distributions for discrete data include:
  Binomial
  Poisson
  Uniform
These distributions can be used to approximate each other given certain conditions
Notes: <number>

## Slide 25: Step 7: The Normal Distribution
The most widely used continuous data distribution
When a variable is continuous, and its value is affected by a large number of chance factors, none of which predominates, then it will frequently have a Normal Distribution
DPMO, process capability, and six sigma calculations are based on the normal distribution
The formula for estimating the area (probability density) is quite complicated, but fortunately there are tables that make the job much easier

x
1
22
-
2
(x – )2
dx
exp
 

## Slide 26: Step 7: The Normal Distribution
Two parameters, X and 
Notes: <number>

## Slide 27: Step 7: The Standard Normal Distribution
No matter what x represents, any normal distribution can be transformed to the standard normal distribution.
The standard normal variable ‘Z’ can be used to calculate the probability density under the curve (See Z tables)
Notes: <number>

## Slide 28: Step 7: Z Tables (One Tail)
1s (68%)
1.96s (95%)
Notes: <number>

## Slide 29: Step 7: Practical Application …
The average number of queries at a trade fair is 3000, and the standard deviation is estimated to be 300.
Total cost is £5,700, normal conversion rate is 5%, with a profit of £50 per job
What is the probability that there will be insufficient jobs generated to cover the cost of attending the fair?
Notes: <number>

## Slide 30: Step 7: Answers
Total cost £5,700, profit per job £50, therefore breakeven is at 114 jobs; this implies 2,280 enquires (114 x 1/0.05)
Enquiries distribution is shown below, the second axis is the equivalent Z score
The area to the left of the z = -2.4 is 0.0082. Therefore we would predict a probability of 0.0082 (or just under 1%) of not breaking even. It is therefore worthwhile taking the stand at the fair
Notes: <number>

## Slide 31: Step 7: The t Distribution
The normal distribution applies to a population
Usually we do not know the value of  and  and are obliged to estimate from a sample
The smaller the sample size the less confident we are of obtaining reliable estimates for the population parameters
To compensate, Z scores can be pushed further out, and the Z score replaced by a t
The distribution changes depending upon the sample size. We need one more parameter, not n, but the degrees of freedom which is n-1
We can now use T tables, in much the same way as Z tables, using an equivalent formula to calculate t:
t = (x – x )
s
Notes: <number>

## Slide 32: Step 7: The t Distribution: Example
t = (4.4 – 5.43)/0.62= -1.66
1.66 is less than 2.201, so at 95% confidence level is consistent with the population from which the sample is drawn.
This is not to say that it is from the parent population, only that fails to provide evidence that it is not
A sample of 12 cases were obtained randomly from different offices.
The case ‘scores’ are:
  4.5, 4.9, 6.6, 5.3, 5.2, 6.1, 5.4, 6.2, 5.2, 4.7, 5.6, 5.5 X= 5.43, s=0.62
A single case lying about is found that has a value of 4.4. Is it Likely that this case represents a population with the same mean as that from which the sample is drawn?
Notes: <number>

## Slide 33: Step 7: The Binomial Distribution
The binomial distribution is appropriate when:
  Observations are counts of things (discrete data)
  An observation can be classified into one of two possible categories e.g ‘number of defective units in a sample’
The binomial distribution is also appropriate when:
  The variance of sample count data is less than the mean
  Objects being counted are dispersed in a regular fashion
Notes: <number>

## Slide 34: Step 7: The Binomial Distribution
Two parameters, n and p
Notes: <number>

## Slide 35: Step 7: The Binomial Distribution
The probability of any number of ‘successes’ can be estimated using the following formula:
P(x) =
p n. q (n-x)
n!
x!(n-x)!
n is the number of trials
p is the probability of ‘success’
q is the is the probability of ‘failure’
Mean = np
Variance = npq
The mean and variance can be shown to be:

## Slide 36: Step 7: Practical Application …
What is the probability of more than three defects in a sample of 12 items if the probability of a defective item is 0.2?
Hint: P(4)+P(5) .. P(12) = 1-[P(0)+P(1) … P(3)]
Notes: <number>

## Slide 37: Step 7: Answers
The required probability is
  P(4)+P(5)+P(6)+P(7)+P(8)+P(9)+P(10)+P(11)+P(12)
  But this may be re-written as 1-[P(0)+P(1)+P(2)+P(3)]
Use the formula to work out the probabilities:
  P(0)= 0.068719477
  P(1)= 0.20615843
  P(2)= 0.283467842
  P(3)= 0.236223201
  Total = 0.79456895
Therefore the the required probability is 1 – 0.79 = 0.21
Notes: <number>

## Slide 38: Step 7: The Poisson Distribution
The Poisson distribution is appropriate when:
  Observations are counts of things (discrete data)
  Counts are obtained from defined sampling units e.g. quadrats, intervals of time etc. and cab organised into a frequency distribution whose mean is approximately equal to the variance
  Objects being counted are ‘rare’ I.e. there are far fewer objects in the sampling unit than it is capable of containing e.g. ‘number of defects per sampling unit’
  Individuals are dispersed randomly in time or space and are independent of one another
Notes: <number>

## Slide 39: Step 7: The Poisson Distribution
One parameter, 
Notes: <number>

## Slide 40: Step 7: The Poisson Distribution
P(x) =
x e-
x!
 is the estimated average
e is a constant 2.7183
=  =  2
 = np
The probability of any number of ‘successes’ can be estimated using the following formula:
The mean and variance can be shown to be:
Notes: <number>

## Slide 41: Step 7: Practical Application …
A call centre receives an average of three calls in a five minute period.
If the company has only four telephone lines, what proportion of customers would not be able to get through during a five minute period?
Hint: P(0)+P(1) …P(4)
Notes: <number>

## Slide 42: Step 7: Answers
If the company has only four telephones, and calls last for five minutes, then the probability of:
  P(0)+P(1)+P(2)+P(3)+P(4)
  0.0498+0.494+0.2241+0.2241+0.168075 = 0.815475
or approximately 0.815 of the switchboard being able to handle all incoming calls
The switchboard is sufficient for 81.5% of the time, but callers are unable to make a connection for 18.5% of the time!
Notes: <number>

## Slide 43: Step 7: Central Limit Theorem
The Central Limit Theorem states that:
“The means of a large number of samples drawn randomly from the same population are normally distributed and the ‘mean of the means’ is the mean of the population”
This ‘magic’ property allows us to make inferences about a population, from a sample, regardless of the actual distribution shape of the population in question
Notes: <number>

## Slide 44: Step 7: Central Limit Theorem
n
SE (standard error of means) = 
Process Mean = X =  (x1+x2+ … xk)
k

## Slide 45: Step 7: Central Limit Theorem -- So What?!
Notes: <number>

## Slide 46: Step 7: Step 7: Central Limit Theorem -- So What?!
The smaller distribution of sample averages provides a useful means of detecting changes in a process.
Any change in the process mean, unless it is extremely large, will be difficult to detect from individual results alone
The SE can be treated as S I.e. normal tables can be used to estimate probabilities in the usual way!!
Notes: <number>

## Slide 47: Step 7: Confidence Intervals
The SE gives us an indication of how good an estimate a sample mean, x, is of a population mean, 
Thus we are 68% confident that  lies within  1 SE of x.
However 68% confidence is a little low we usually want to be more sure that a population lies between indicated limits (usually 95% or 99%)
These can be obtained by multiplying the SE by the appropriate Z or t scores
Notes: <number>

## Slide 48: Step 7: Confidence Intervals for Means
CI for Large (n>30) Samples:
 = x  Z.SE
Typical Z Values
Z95 = 1.96
Z99 = 2.58
CI for Small Samples:
x  t.SE
Notes: <number>

## Slide 49: Step 7: Confidence Intervals for Percentages
CI for Large Samples (n>30):
CI for Small Samples:
n
 = p  t(p(100-p)
n
 = p  Z(p(100-p)
Notes: <number>

## Slide 50: Step 7: Exercise to Demonstrate Confidence Intervals
A sample of 90 people were were selected from a large population. If the average amount spent per week on a product was found to be £5.60, and the sample standard deviation was found to be £2.90, calculate the 95%CI for the mean of the population.
A random sample of 100 invoices has been selected from a large file of company records. If nine were found to contain errors, calculate a 95%CI for the true percentage of invoices in the company containing errors
Notes: <number>

## Slide 51: Step 7: Answers
CI for a mean:
 = £5.60  1.96 x £2.90/ 90 = £5.60  £0.599
CI for a percentage:
 = 9%  1.96 x  [(9(100-9)/100] = 9%  5.609%
Notes: <number>

## Slide 52: Step 7: Process Capability and Control
Time to take stock:
  We know how to interpret measures of location and variation for our data sample
  We can make inferences about the true population parameters from our samples
  We know how to use distributions to calculate the probability of events concerning our population for business case and Risk scenarios
Now we need to ask:
  Is the process in control?
  How well does the process meet, or not meet its requirements?
Notes: <number>

## Slide 53: Step 7: Capability Indices
In order to deliver an output or service within a specification, the difference between the Upper Specification and the Lower Specification must be less than the total process variation
So a comparison of 6 with (USL - LSL) or 2T gives an obvious process capability index, known as the CP of the process:
Cp =
USL-LSL
6
OR
Cp =
2T
6
Notes: <number>

## Slide 54: Step 7: Capability Indices – Cp
If the process is not centred then it is possible that a significant proportion of the population is outside of the specification.
This does not invalidate the use of Cp to measure potential capability, but rather that we need another measure to take into account centring
Notes: <number>

## Slide 55: Step 7: Capability Indices for Centring
Cpk takes into account both the process variation and the centring
For USL and LSL there are two Cpk values, Cpku and Cpkl
These relate the difference between the process mean and the USL and LSL respectively, to 3 (half the total variation)
The overall Cpk is the lower value of Cpku and Cpkl
Cpku =
USL-X
3
Cpkl =
X-LSL
3
Cpk =
Min {Cpku,Cpkl }
Notes: <number>

## Slide 56: Step 7 : Capability Indices – Cpk
The Cp tells us the process could potentially be very capable
However, the Cpk tells us the process is not centred, is capable wrt to the LSL, but not capable wrt the USL
Notes: <number>

## Slide 57: Step 7: Interpreting Capability Indices
  Cpk < 1 Not capable and there will be non-conforming output from the process
  Cpk = 1 Not really capable, any slight change may lead to non-conforming output
  Cpk = 1.33 Still not really acceptable, changes still may not be detected by SPC charts*
  Cpk = 1.5 Better but still not great
  Cpk = 1.67 Promising, non-conforming output will occur but there is a good chance it will be detected
  Cpk = 2 High level of confidence in producing conforming output
Notes: <number>

## Slide 58: Step 7: Capability Indices Notes
The data should be normally distributed If not use an indices based on the appropriate model
The process should be in control before you attempt to determine the capability
If your process is not in control the validity of Cpk is questionable
The  used for Cpk is an estimate based on the range of samples. If you want to use the normal  based on individuals the index becomes Ppk
The difference is that Cpk indicates what the process is capable of, Ppk indicates how the process is currently performing
Notes: <number>

## Slide 59: Step 7: Defects per Million Opportunities (DPMO)
The DPMO and the related Sigma Level are classic ‘Six Sigma’ measures that allows process performance to be compared throughout an entire organization, because they are independent of the process.
DPMO is merely a determination of opportunities and defects, however the terms are appropriately defined for that specific process.
Notes: <number>

## Slide 60: Step 7: DPMO Template
Number of units processed N = __________
Total number of defects made
(include defects made and later fixed) D = __________
Number of defect opportunities per unit (equate to CTQs) O = __________
Calculate # defects per million
Opportunities DPMO = 1,000,000 x (
= 1,000,000 x
= __________
Look up process sigma in
sigma conversion table (or z tables) Sigma = __________
D
N x O
)
( )
( ) ( )
Notes: <number>

## Slide 61: Step 7: Six Sigma Tables
The Sigma Level is just a Z score (one tail)
The yield is a probability density
Most tables automatically include a 1.5 shift
Notes: <number>

## Slide 62: Step 7: The Problem...
Scale
Time
The Horror! We were doing
so well now its all gone so wrong!!
We must make a
change immediately!!
Week 1
Week 2
Week 3
Notes: <number>

## Slide 63: Step 7: The Problem...
Scale
Time
Hmmm ...
over-all there was no real change
in our performance. Was I wrong to
worry about it in Week 3, Month 1??
Month 1
Month 2
Month 3
Same Point

## Slide 64: Step 7: Process Variation
Methods
Technology
People
Environment
X
Y
Distribution of measured process characteristic

## Slide 65: Step 7: Process Variation
Two types of variation:
Common Cause variation is always present to some degree and is caused by interactions of multiple factors
Special Cause variation means something different happened at a certain place or time
Notes: <number>

## Slide 66: Step 7: Let’s Hear It for Walter
Back in the 1920’s, Walter Shewhart wanted to find a way to understand variation more effectively
He wanted to identify the difference between natural and special cause variation
Shewhart felt too much time was being wasted by mistaking the two. And these mistakes are important
Notes: <number>

## Slide 67: Step 7: Getting Common and Special Mixed
Mistake common for special cause variation ...
Result
Tampering – leading to increased variation
Mistake special cause for natural variation …
Result
Missed or delayed opportunity to improve
Notes: <number>

## Slide 68: Step 7: So How Do We Know?
Shewhart ran thousands of experiments …
He found that by introducing ‘control limits’ placed at plus and minus three standard deviations from the mean, he could minimise the chances of mistaking the two
The data within the control limits was almost always natural variation; the data outside the control limits was almost always special cause variation
Notes: <number>

## Slide 69: Step 7: It Works!
Theoretically, at plus and minus three standard deviations from the mean, the control limits will contain 99.73% of the natural results of the process, but …
This isn’t why he chose plus and minus three standard deviations as the optimum position for the control limits
He chose them because they work!
Notes: <number>

## Slide 70: Step 7: Process Variation: Common Cause
Common Causes are due to the input and process variables that contribute to the regular everyday variation in the process
  Common to all occasions and places
  Degree of presence varies
  Each cause contributes to the output
A process with only common cause variation is referred to as stable
Notes: <number>

## Slide 71: Step 7: Process Variation: Common Cause
X
UCL
LCL
Scale
Notes: <number>

## Slide 72: Step 7: Step 7: Process Variation: Special Cause
Common Causes are not always present in the process but appear because of some particular circumstance
  Not always present
  Temporary or local
  Can’t predict when or where it will occur
A process with only special cause variation is referred to as unstable
Notes: <number>

## Slide 73: Step 7: Process Variation: Special Cause
LCL
X
UCL
Scale
Notes: <number>

## Slide 74: Step 7: Control Charts
Run charts with control limits calculated and displayed
Two types:
  Variables (measured data) e.g. call handling time
  Attributes (count data) e.g. number of dropped calls
Notes: <number>

## Slide 75: Step 7: Control Charts: Variables Control Chart
Normal variation due to chance
Abnormal variation due to assignable sources
Abnormal variation due to assignable sources
Out of control
X
UCL
LCL
Scale
Sample no.

## Slide 76: Step 7: Observations from Sample Distribution
X
UCL
LCL
Scale
Notes: <number>

## Slide 77: Step 7: Accuracy and Precision
Increased Accuracy
Increased Precision
Notes: <number>

## Slide 78: Step 7: Mean and Range Charts
Mean charts (X-Charts):
  Plot the sample mean against the process mean.
  Detect changes in process accuracy
Range charts (R-Charts):
  Plot the sample range against the mean process range
  Detect changes in process precision
Notes: <number>

## Slide 79: Step 7: Mean and Range Charts
X-Chart detects changes in process accuracy...
UCL
X
LCL
UCL
X
LCL
X-Chart
R-Chart

## Slide 80: Step 7: Mean and Range Charts
R-Chart detects changes in process precision...
UCL
X
LCL
UCL
X
LCL
X-Chart
R-Chart

## Slide 81: Step 7: Control Charts for Attributes
p and np charts:
  For binomial distributed data
    p-Chart used to monitor the proportion of defectives in a process
    np used to monitor the number of defectives in a process
c and u charts:
  For the Poisson distribution
    c-Chart used to monitor the number of defects (count)
    u-chart used to monitor the number of defects per unit
Notes: <number>

## Slide 82: Step 7: Use of p-Charts
When observations can be placed into two categories:
  Pass or Fail
  Yes or No
Monitors the fraction defective in varying sample sizes
np-charts monitor the fraction defective in constant sample sizes
Notes: <number>

## Slide 83: Step 7: Use of c-Charts
Use only when the number of occurrences per unit of measure can be counted and non-occurrences cannot be counted:
  Errors per item
  Faults per unit
  Calls or complaints per unit of time
  Number of muggings reported each year
Notes: <number>

## Slide 84: Step 7: Monitoring Improvements
UCL
LCL
X
Process not centred and not stable
Process centred and stable
Process improved
X

## Slide 85: Step 7: Out of Control Conditions1
One or more points either above the UCL or below the LCL
Eight or more consecutive points either above or below the centre line
Six or more consecutive points showing a continuous increase or decrease
Fourteen or more points oscillating back and forth
1- Taken from ‘Quality and Statistical Process Control’, S. Sytsma, Ferris State University
Notes: <number>

## Slide 86: Step 7: Flowcharts for Components of Variance
np-Chart
p-Chart
c-Chart
u-Chart
Defectives
or Defects
Defectives
Defects
xr-Chart
xs-Chart
i-Chart
Sample
Size
>1
=1
Range or s
Range
s
Constant
Sample
Size
Constant
Variable
Constant
Sample
Size
Constant
Variable
Start
Type of
Data
Variables
Attributes

## Slide 87: Step 7: Calculating Control Limits
Distribution | Chart | Control Limits | Comments
Binomial | p chart | p  3  p(1-p)/n | n is the number of units per subgroup, p is the proportion of defectives
Binomial | np chart | np  3  np(1-p) | np chart is used when n is roughly constant
Poisson | c chart | c  3  c | c is the count of defects. Use when area of opportunity is constant)
Poisson | u chart | u  3  u/a | u=c/a where, c is the count of defects, and a is the area of opportunity
Normal | i chart | x  A2R For range chart UCL= R.D4 LCL= R.D3 | R is the average range A2, D3, and D4 are constants (A2 =2.66, D4 = 3.267, D3 = 0 for i charts)
Normal | XR chart | x  A2R For range chart UCL= R.D4 LCL= R.D3 | R is the average range (needs to be estimated) A2, D3, and D4 are constants that vary with sample size
If you want to use SPC then it is highly recommended you read a good book on the subject! Try Paul Oakland's ‘SPC Handbook’
Notes: <number>

## Slide 88: Step 7: Statistical Process Control -- Final Thoughts
Although SPC is a great tool there are several things to consider:
  SPC really comes into its own during the control phase,after you’ve removed the special causes of variation as a process management tool (we’ll talk about this during the control stage)
  SPC will probably identify that the process is out of control during the analyse stage
  To use SPC effectively the process owners have to be disciplined in data collection, and on-going process management
Notes: <number>

## Slide 89: Analyse Steps
Step 7:
Baseline Process Performance (Y)
Step 8:
Identify Significant Variables (xs)
Step 9:
Explore Root Causes of Significant Variables (xs)
Toll Gate Review
Notes: <number>

## Slide 90: Step 8: Verifying the Causes
Our process models, I/O, Ishikawa etc. have hopefully done a good job in identifying the potential causes (xs)
We have collected data around some of xs we need to know more about
We know need to explore this data to verify which have the greatest influence on the main project Ys
Notes: <number>

## Slide 91: Step 8: Key Outputs
In completing step 8, you should produce at least the following:
  A report on the contribution each potential root cause has on the project Ys
  A recommendation as to which root causes need to be addressed by any future solutions
Notes: <number>

## Slide 92: Step 8: Possible Tools
A few tools are applicable to this step:
  Graphical Analysis
  Process Analysis
  Hypothesis Testing
  Design of Experiments (DOE)*
DOE is a tool one can use to explore the interaction between the xs and their effect on the Y. Used correctly it can actually allow you to calculate the transfer function.
However, its use is limited in transactional / service processes where variables are hard to control. It is much better suited for manufacturing processes. We will look at DOE in the ‘Improve’ Stage where it can also be used to test various solutions
Notes: <number>

## Slide 93: Step 8: Graphical Analysis
There are many different ways to display data that help highlight relationships between variables and / or help identify the critical variables.
Common tools include:
  In Time:
    Discrete:
      Histograms
      Pie Chart
      Pareto
    Continuous:
      Box Plot
      Scatter Plot
  Overtime:
      Control Chart
      Run Chart
Notes: <number>

## Slide 94: Step 8: Pareto Diagrams
Pareto charts help you analyse discrete data.
It is a graphical tool that helps you break a big problem down to its constituent parts and identify those parts which, if fixed, have the greatest potential for improvement
Steps for Pareto Chart:
  Decide on the situation or process of interest
  Choose discrete categories to monitor
  Gather the data
  Sort the discrete categories by frequency in descending order
  Calculate the cumulative sum (CUSUM)
  Plot the data and interpret the results
Notes: <number>

## Slide 95: Step 8: Pareto Diagrams
The Pareto principle states that 80% of the problems are caused by 20% of the contributors
This implies we can frequently solve a problem by identifying and fixing the vital few causes
Depending upon the level of stratification you’ve selected, one can drill down through the major contributing categories until Pareto principle can be shown to apply and causes o variation are identified
Notes: <number>

## Slide 96: Step 8: Interpreting Pareto Diagrams
Notes: <number>

## Slide 97: Step 8: Interpreting Pareto Diagrams
Pareto principle applies
Focus improvement effort on top two bars
Pareto principle does not apply
Look for other ways to categorise the data and/or look for other root causes
Notes: <number>

## Slide 98: Step 8: Scatter Plots
Is a graph that helps visualise the relationship between two variables (e.g. the Y and a potential x)
Specifically they may identify if there is a cause-and-effect relationship (but finding a relationship does not always imply causation)
A scatter diagram is a precursor to correlation and regression hypothesis tests
Notes: <number>

## Slide 99: Step 8: Steps to Create Scatter Plots
Collect paired data along with other information (e.g. stratification data elements)
Determine which variable is the independent variable, the other(s) should be dependant on the independent variable
Plot the data, independent variables on the X axis (the causes?), dependant variables on the Y axis (the effect)
Check for outliers, what do they signify, if anything?
Interpret the pattern formed by the scatter of plots
Perform a correlation analysis if it looks like there is a relationship
Notes: <number>

## Slide 100: Step 8: Interpreting Scatter Plots
Strong Positive Correlation
Strong Negative Correlation
Possible Positive Correlation
Possible Negative Correlation
Other Pattern
No Correlation
Notes: <number>

## Slide 101: Step 8: Interpreting Scatter Plots
All Data
Stratified Data
Stratification can reveal cause-and-effect relationship previously hidden
Notes: <number>

## Slide 102: Step 8: Warning! Correlation Does Not Imply Causation
Number Of Storks
50
100
80
70
60
200
300
50
80
70
60
100
200
300
Source: Box, Hunter, Hunter. Statistics For experimenters. New York, NY: John Wiley & Sons. 1978.
Human Population (In Thousands)
Notes: <number>

## Slide 103: Step 8: Quantifying The Strength Of The Relationship
The correlation coefficient r measures the strength of linear relationships
Perfect negative relationship r = – 1 no linear correlation r = 0 perfect positive relationship r = + 1
By expressing r2 as a percentage, we measure the percent of variation in Y explained by the linear relationship of X and Y
So, if r = 0.8, for example, r2 = 64%
Notes: <number>

## Slide 104: Step 8: Process Analysis
Process analysis helps identify critical processes or process inputs that contribute to the main process outputs
Common tools include:
  Value Stream Analysis
    Q-labels
    Value Stream Mapping & Time Value Mapping
    VA/NVA/BVA analysis & Process Characterisation
  Activity Based Costing
    Resource process costs (FTE)
    Material costs
    Unit costs
    Process Characterisation
These tools require a process model as a point of reference
Notes: <number>

## Slide 105: Step 8: Uses of Value Stream Analysis
Makes the ‘invisible’ visible
  Shows where time is being spent
  Pin-points the biggest time traps
Pre-cursor to activity based costing
  Provides the data to develop costing model
  Helps quantify opportunity costs, or the cost-of-poor-quality
Major tool for ‘lean’ thinking
  Helps identify process capacity
  Helps quantify required resources and utilisation
  Quantifies process efficiency
  Target reduction in large WIP concentrations to reduce capital costs (manufacturing) and reduce lead time
If you are not interested in timings (or ultimately costs) don’t do a value stream analysis
Notes: <number>

## Slide 106: Step 8: Quantification Labels
Derived
AR = .f-1
CR = R  R.R (Round Down).[PT]-1
Ut. = (PT x  [per unit time])  (R x AVT)
PE (Services) = PT  CT
PE (Manufacturing) = Value added time  LT
LT = WIP  CR
Annotate IDEFØ or Flow Block Diagrams with relevant Q-Labels
RESOURCES
SR = Units of resource and type
R.R = No. of resources required per unit
AVT = Available time per resource
Ut. = Resource Utlisation (%)
Rel. = % Reliability of equipment
INPUT
S = Input volume and type
f = Frequency of input
AR = Arrival Rate (or Demand Rate)
QT = Queuing time
TT = Transition time
%C&A = % Complete and Accurate
PROCESS
WIP = Work in Process
CT = Process cycle time
PT = Process execution time
LT = Process lead time
CR = Completion Rate
PE = Process Efficiency (%)
OUTPUT
WT= Weighting
FR = Flow Rate
It = No. of Iterations (feedback)
Process
Input A
Input B
Resources
Output A
Output B
Notes: <number>

## Slide 107: Step 8. Traditional VSM
Traditional VSM symbols are oriented to manufacturing production systems. If you use traditional symbols for service environment: material flows are the actual flow of data, Information flows are scheduling, sequencing or controlling data (NB. Think IDEFØ!)
Notes: <number>

## Slide 108: Step 8. Value Stream Mapping (VSM) & Time Value Mapping (TVM)
NVA (PT)
VA (PT)
VSM
TVM
PE < 2%
NVA (TT)
NVA (QT)
Notes: <number>

## Slide 109: Step 8: CT and PT for Transactional / Service Processes
Notes: <number>

## Slide 110: Step 8: VA/NVA Analysis & Process Characterisation
  Characterise processes in terms of them adding value to the product
  Characterise processes in terms processing type
  Express value types and processing types as % of total cycle or total processing time
Example Processing Types
Data Entry
Rules Based Processing
Automated
Decision Making
Manual Preparation
Checking
Filing
Comms
Notes: <number>

## Slide 111: Step 8: Building a Value Stream Map
Determine approach for multiple product /service families and re-work:
  Separate models
  Multiple Q-Labels / line items per process
  Extra process boxes – work forward in time*
Identify required metrics
Prepare process model for VSM:
  If IDEFØ remove controls, create ‘missing’ Inputs
  If Flow Block identify input units for each process step
  Create extra processes and re-wire as appropriate
  Define work-flow logic (logic junctions are very useful)
  Ensure one work unit type per process (NB. can stratify)
Collect data
Complete model & provide a tabular summary
Notes: <number>

## Slide 112: Step 8: It’s as Easy as ABC …
A form of cost accounting that focuses on the costs of performing specific functions (processes, activities, tasks, etc.) rather than on the costs of organizational units.
  Generates more accurate cost and performance information related to specific products and services than is available to managers through traditional cost accounting approaches.
  Captures the current cost of performing an activity
  Targets High Cost activities
  Allows to cost out measurements to business simplification and process improvement
  Enable quantification of opportunity costs, and/or the cost-of-poor-quality for developing a business case
  Provides a context for establishing and monitoring performance measures
  Provides the link between activity modelling and economic analysis
If you started the ABC during the define stage, the result form this form of analysis can be very powerful in identifying the real cost drivers
Notes: <number>

## Slide 113: Step 8: Activity Based Costing (ABC): Simple
The following method is for a very quick, high level estimate:
  Estimate the full time equivalent (FTE) per process (ask resources)
  Estimate the input volume () and frequency (f) for each process (ask resources/sample/check records)
  Estimate annual purchase costs per process (ask accountant)
  Derive annual labour costs per process = FTE x fully loaded payroll cost (FLPC) (ask accountant)
  Derive total annual costs per process = Annual labour Costs + annual purchase costs
  Derive unit cost per process = Annual total cost ÷ Annual Input volume
Notes: <number>

## Slide 114: Step 8: Activity Based Costing (ABC): Enhanced
To improve the estimations:
  Derive the (FTE) per process = ((PT per Input Unit x  Input Volume) ÷ Time Available per Resource) x Resources Required per Unit)
  Create separate models / entries for best, worst and most likely cases
  Instead of averaging FLPC, calculate the direct contribution of each resource
  Collect real data
Notes: <number>

## Slide 115: Step 8: Hypothesis Testing
Hypothesis testing aims to make statements about a population parameter, or parameters based on the basis of sample evidence
We look to see if a set of sample results support or are consistent with some fact or supposition about a population. We look to get a ‘yes’ or ‘no’ answer from a significance test; either the results support the supposition or they do not
As you might expect the ideas of confidence intervals and significance tests are closely linked
We can extend the concept; we may have a set of samples from 2 or more processes and want to test if there is a significant difference between the averages
Notes: <number>

## Slide 116: Step 8: Hypothesis Testing
Hypothesis tests can be used to to see if there are differences between:
  Averages, either between samples, or a sample and a target value
  Variances between samples, or a sample and a target value
  Proportions either between samples, or a sample and a target value
  Distribution of a sample against a known distribution (e.g. checking for ‘normality’
Notes: <number>

## Slide 117: Step 8: Hypothesis Testing
Examples of Hypothesis Tests:
Type of Data | What you can Compare | Example
Discrete | Proportions | Is the % of first-time AML checks for Office a the same as for Office B?
Continuous | Averages | Has the cycle time improved between the ‘old’ process and the ‘new process?
 | Variation | Do results from the group using the new method vary less than the results from the group using the old method
 | Shapes or Distributions | Are cycle-time normally distributed, or do they fit a Weibell model?
Notes: <number>

## Slide 118: Step 8: Hypothesis Testing – How Does it Work?
Because of variation, no two anythings will be alike
The question is whether differences you see between samples, groups, processes, etc., are due to random, common cause variation, or if there is a real difference
Various hypothesis tests provide ways of estimating common cause variation for different situations
They test whether a difference is significantly bigger than the common cause variation we would expect for the situation
If the answer is no, there is no statistical difference (although there may be practical one!). If the answer is yes, conclude that the groups / sample is different
Notes: <number>

## Slide 119: Step 8: Steps in Performing a Hypothesis Test
Select the Test
State the hypothesis (H0 and Ha)
State the significance level ()
State the critical (cut-off) values (e.g Z, t scores)
Calculate the test statistic
Compare test statistic to the critical values
Come to a conclusion (Accept or reject H0)
Put your conclusions into English

## Slide 120: Step 8: Select the Test

## Slide 121: Step 8: Making a Hypothesis
The supposition we wish to test is called a hypothesis. We actually have two hypothesis, the first or null hypothesis (H0) is that there has been no change to the parameter that we are testing form that which previously existed
The Alternative hypothesis (H1 or Ha) is that the null hypothesis is not true; there is in fact a significant difference

## Slide 122: Step 8: Making a Hypothesis – How Many Tails?
Two-tailed tests are used to determine if a parameter such as the average or variance is equal to a specific value:
  H0:  = 0 (or H0: 1 = 2)
  Ha:   0
With one-tailed tests, one of two possible alternative hypotheses must be selected. The alternative hypothesis is stated as an inequality; either greater than or less than:
  H0:  = 0 (or H0: 1 = 2)
  Ha:  > 0 or Ha:  < 0
NB. In 99% of cases use a two-tailed test*

## Slide 123: Step 8: The Critical Value – Decision Errors
Since the decision to accept or reject H0 is based on a sample estimate, it is possible to arrive at an incorrect decision. The two types of errors that can occur when performing a hypothesis test are referred to as Type I and Type II errors:
NO
ERROR
Type II
ERROR
Type I
ERROR
NO
ERROR
Accept H0 –
Groups are the Same
Reject H0 –
Groups are the Different
Groups are the Same
Groups are the Different
Actual Truth
Conclusion or Decision

## Slide 124: Step 8: The Critical Value – Decision Errors
Type I Error
This type of error occurs when we reject H0 when it is true. The probability of committing a type I error is called alpha () risk
  We can control  directly because we specify the significance level of the test (e.g. 95%)
Type II Error
This type of error occurs when we accept H0 when it is not true. The
probability of committing a type II error is called beta () risk
  We cannot directly control the power of the test because  is influenced by sample size. The larger the sample becomes the smaller is our  risk with a corresponding increase in power of the test

## Slide 125: Step 8: Decision Rules
The decision to accept or reject H0 depends upon the value of our parameter estimate relative to the distribution parameter (e.g. z-value, t-value, 2 value) that corresponds to the significance level we have chosen (normally 95%).
The significance level is equal to  for one tail tests, or /2 for two tail tests

## Slide 126: Step 8: Decision Rules -- Example
Two-Tailed Hypothesis Test
One Tailed Hypothesis Test
Greater Than Alternative
One Tailed Hypothesis Test
Less Than Alternative

## Slide 127: Step 8: Hypothesis Tests of the Mean (Sample vs Target)
Z-Test is used to compare a sample average to a specified value when the is known.
  H0:  = 0
  Ha:   or < or > 0
The formula should be familiar to you:
n

Z = x - 
If the is unknown, use the t-test, again the formula should be familiar to you:
n
s
t = x - 

## Slide 128: Step 8: Exercise …
An operational manager claims than an average of 50 claims per hour are completed be his team. A random sampling of 48 different claim handlers at different times shows an average of number completed to be 47.5, with a standard deviation of 0.7 claims. Does this evidence support the assertion by the manager at the 5% level of significance?
Alpha Risk | 2-Tailed Z-Value (/2) | 1-Tailed Z-Value () | Confidence level
0.100 | 1.64 | 1.28 | 90%
0.050 | 1.96 | 1.64 | 95%
0.025 | 2.24 | 1.96 | 97.5%
0.010 | 2.58 | 2.33 | 99%

## Slide 129: Step 8: Answers …
Step 1:
  H0:  = 50
  Ha:   50
Step 2:  = 5% (stated in question)
Step 3: Critical values = -1.96 and +1.96 (two-tailed)
Step 4: Test Statistic = Z = (47.5 – 50) / (0.7 /48) = -24.744
Step 5: The test statistic (-24.744) is below the critical value (-1.96)
Step 6: Reject H0 at 5%
Step 7: The operational manager is a liar! The number is significantly different from 50!

## Slide 130: Step 8: Hypothesis Tests of the Mean (Two Samples)
Z-Test is used to compare the means of two samples when their sare known.
  H0: 1 - 2 = 0
  Ha: 1 - 2  0 (or 1 > or < 2 )
The formula should be familiar to you:
If the sare unknown, use the t-test:
Z = ( x1 – x2 ) – (1 - 2)
n1
2

2
n2

t = ( x1 – x2 )
n1
1

1
n2
Sp
Sp is the pooled standard error
Degrees of freedom (n1+n2-2)
Sp =  (n1-1)s12 + (n2-1)s22
n1+n2-2
As H0 says that the two populations means are equal we can remove remove 1 - 2 from the equation

## Slide 131: Step 8: Exercise …
A company has two offices one is Spain, one in the UK. The Head office feels the Spanish Office is more efficient, and take a sample form each to test the assertion. The UK office samples 20 workers and finds it takes 25 mins to complete a standard task, with a standard deviation of 5 mins. The Spanish office samples 10 workers, and finds it takes 20 mins to complete a standard task, with a standard deviation of 4 mins. Does this evidence support the assertion at the 1% level of significance, that Spanish workers are more efficient?

## Slide 132: Step 8: Answers …
Step 1:
  H0: (1 - 2) = 0
  Ha: (1 - 2) > 0
Step 2:  = 1% (stated in question)
Step 3: Degrees of freedom = 20 + 10 – 2 = 28, Critical values = 2.467 (one-tailed)
Step 4:Test Statistic
Sp = [(19 x 52) + (9 x 42)/ (20 + 10 – 2)] = 4.70182
t = 25-20/Sp[1/20+1/10] = 2.746
Step 5: The test statistic (2.746) is above the critical value (2.467)
Step 6: Reject H0 at 1%
Step 7: The Spanish are more efficient than the British!

## Slide 133: Step 8: Matched Pairs
A special case arises when we are considering tests of the differences of means if the two samples are related in such a way that we may pair the observations e.g:
  Two employers score the same candidate
  You wish to compare two different calculation methods on the same item to see if there is a difference
The hypothesis is that no difference exists between the means:
  H0:  = 0
  Ha:   0
The formula looks at the average distance against the hypothesised difference, and divides by the standard error of the paired differences
t = d – 
Sd
d is the average distance between sample pairs
Sd is the standard error of the paired distances

## Slide 134: Step 8: Matched Pairs -- Example
Sample 1 | Sample 2 | Difference
92.3 | 93.2 | 0.9
90.5 | 83.7 | -6.8
91.9 | 90.8 | -1.1
91.7 | 91.8 | 0.1
94.9 | 88.7 | -6.2
93.6 | 90.7 | -2.9
90.5 | 93.8 | 3.3
93.3 | 91.0 | -2.3
94.4 | 91.3 | -3.1
 | d = | -2.0
 | Sd = | 3.3
H0:  = 0
Ha:   0
Alpha = 0.05
df = 18
t(/2) = 2.11
t = -2.0 – 0 = -1.86
3.3/  9
Since –1.86 < 2.11 we accept H0.
There is no difference between the samples

## Slide 135: Step 8: Hypothesis Tests of Proportions
Hypothesis tests can also be used for proportions. This time though we use the binomial distribution to calculate the test statistic.
As before proportion tests can be used to detect:
  Significant differences between a sample proportion and a specific target proportion
  Significant difference between two sample proportions

## Slide 136: Step 8: One Sample Proportion Tests
The single proportion test is used to compare a binomial proportion to a specific value.
  H0:  = 0
  Ha:   or < or > 0
The formula is:
Z = p - 0
n
0 (100- 0 )
p is the sample percentage
 is the claimed population percentage (remember that we are assuming the that the null hypothesis is true)
As before, for small samples (n<30) use t tables instead of Z tables, for n-1 degrees of freedom:

## Slide 137: Step 8: Exercise …
A company expects to get 20% of the market share with its new product. A small product trial against competing brands from 200 potential customers found that 44 would buy the product as opposed to the competition.
Test if this figure is above the expected market share at the 5% level
Alpha Risk | 2-Tailed Z-Value (/2) | 1-Tailed Z-Value () | Confidence level
0.100 | 1.64 | 1.28 | 90%
0.050 | 1.96 | 1.64 | 95%
0.025 | 2.24 | 1.96 | 97.5%
0.010 | 2.58 | 2.33 | 99%

## Slide 138: Step 8: Answers
Step 1:
  H0:  = 0
  Ha:  > 20%
Step 2:  = 5% (stated in question)
Step 3: Critical values = 1.645 (one-tailed)
Step 4:Test Statistic
Sample percentage = 44/200 x 100 = 22%
Test Statistic = z = 22 – 20 / [20/(100-20)/200] = 0.7071
Step 5: The test statistic (0.7071) is below the critical value (1.645)
Step 6: Cannot reject H0 at 5%
Step 7: There is no evidence that the new product will do better than the company’s claim

## Slide 139: Step 8: Two Sample Proportion Tests
The two sample proportion test is used to perform a binomial comparison between two samples:
  H0: 1 = 2 (or 1 - 2 > or < x%)
  Ha: 1  or < or > 2
The formula is:
Z = (p1 – p2) – (1 - 2)
n1
1 (100- 1 )
n2
2 (100- 2 )
+

[
]
If H0 is 1 - 2 = 0 then we can remove 1 - 2 from the equation

## Slide 140: Step 8: Exercise …
A company believes that a new promotional campaign will increase favourable perceptions of a product by 20%. Before the campaign, a random sample of 500 customers showed that 20% had favourable attitudes to the product. After the campaign, a second random sample of 400 showed 28% had favourable reactions. Use an appropriate test at the 5% level of significance to find if there has been a 10% improvement in favourable perceptions
Alpha Risk | 2-Tailed Z-Value (/2) | 1-Tailed Z-Value () | Confidence level
0.100 | 1.64 | 1.28 | 90%
0.050 | 1.96 | 1.64 | 95%
0.025 | 2.24 | 1.96 | 97.5%
0.010 | 2.58 | 2.33 | 99%

## Slide 141: Step 8: Answers
Step 1:
  H0: (2 - 1) = 10%
  Ha: (2 - 1) < 10%
Step 2:  = 5% (stated in question)
Step 3: Critical values = -1.645 (one-tailed)
Step 4:Test Statistic = z = (28 – 20) – (10) / [(20/(100-20)/500) + (28/(100-28)/400)] = -0.697
Step 5: The test statistic (-0.697) is above the critical value (-1.645)
Step 6: Cannot reject H0 at 5%
Step 7: The sample supports a 10% increase in favourable views

## Slide 142: Step 8: Enough Statistics!!
We’ll stop the stats there! Hopefully, the concept and general approach to hypothesis testing makes sense and its application is understood
Other types of common tests include:
  ANOVA: as Z or t tests but when you want to look at the averages of more than two samples, or even factors (2 way or nested ANOVA)
  2 tests: as proportion tests but when you want to look at more than one factor. Uses the 2 distribution to test observed vs. expected frequencies
  Non-parametric tests: similar to z or t tests but compare medians. Use when the data is not normally distributed (distribution free). Common tests include Mann Whitney, Kruskal wallis, Moods Median
  Variance tests: test if sample population have equal variances (or vs. an expected value). Most parametric tests assume equal variance, or need to be modified if variances are not equal. A 2 is used for tests vs a specific value, a variety of F tests for comparing two or more samples
  Tests for distribution: a normality test is often done prior to any parametric test as the assumption is the populations are normally distributed. Common normality test is the Anderson Darling, but a 2 is a bonafide alternative
  Correlation: a measure (-1 to +1) to see how well correlated two variables are. Several methods can be used depending upon if the data is on an ordinal or interval scale (Spearman’s Rank, Product Moment Coefficient). Correlations scores can also be tested for significance
  Regression: a regression equation can be derived for two or more variables. Should be done after a correlation analysis. Several types increasing in complexity – Linear, multiple etc.

## Slide 143: Analyse Steps
Step 7:
Baseline Process Performance (Y)
Step 8:
Identify Significant Variables (xs)
Step 9:
Explore Root Causes of Significant Variables (xs)
Toll Gate Review

## Slide 144: Step 9: Coming to a Conclusion
We’ve now isolated a few critical xs that we’ve proven through factual data analysis are major contributors to the overall process output variable (Y)
We now need to:
  Firstly explore the differences between the groups and list all possible underlying root causes.
  Secondly, validate the possible underlying root causes and evaluate their impact on the project CTQs
  Finally prioritise the identified root causes based on their impact.

## Slide 145: Step 9: Possible Tools
A few tools are applicable to this step:
  CE Analysis (Fishbone/Ishikawa)
  5 Whys
  Criteria Based Matrix
  Design of Experiments (DOE)

## Slide 146: Step 9: Root Cause Analysis
The old faithful Ishikawa analysis is a good tool to identify the potential underlying root causes.
Just put the significant variable in the effect portion of the fishbone diagram

## Slide 147: Step 9: 5 Whys?
The 5 whys typically refers to the practice of asking, five times, why the failure has occurred in order to get to the root cause/causes of the problem
This techniques works well with the Ishikawa technique; ask the 5 whys every time you identify a new root cause

## Slide 148: Step 9: 5 Whys?
An example is in order:
  You are on your way home from work and your car stops:
  Why did your car stop? Because it ran out of petrol
  Why did it run out of gas? Because I didn't buy any petrol on my way to work.
  Why didn't you buy any petrol this morning? Because I didn't have any money.
  Why didn't you have any money? Because I lost it all last night in a poker game.
Daft example but it should illustrate the importance of digging down beneath the most proximate cause of the problem. Failure to determine the root cause assures that you will be treating the symptoms of the problem instead of its cause, otherwise you will continue to have the same problems over and over again.
Note that the actual numbers of whys is not important as long as you get to the root cause. One might well ask why did you lose all your money in the poker game last night?

## Slide 149: Step 9: Criteria Based Matrix
A criteria based matrix similar to the one you may have used during the define step:
  Define the criteria you think is important for prioritising the variable, usual suspects are the Ys, cost, ease of solving, risk propensity etc.
  Weight the criteria (uses AHP* if you like)
  Score the variables either directly (or using AHP*) against the criteria
  Come to a conclusion as to the relative importance of each variable
We will cover the Analytic Hierarchy Process (AHP) in the ‘Improve’ phase

## Slide 150: Analyse Summary
Step 7:
Baseline Process Performance (Y)
Step 8:
Identify Significant Variables (xs)
Step 9:
Explore Root Causes of Significant Variables (xs)
Toll Gate Review

## Slide 151
www.BeyondLean.com
Thank You!