## Slide 1: Lean Six Sigma Certification & Training
Module 002 Section 003
Failure Mode and Effects Analysis - FMEA

## Slide 2: Application Examples
Design: A designer needs to design a brake pad for a new caliper assembly. How do we identify the effect the new brake pad will have on the caliper assembly
Discrete Manufacturing: A new screw machine with improved capability is going to be added to the manufacturing floor. What effect will this have?
Continuous Manufacturing: A laminate customer has added a requirement for particulate contamination; how do we plan to measure and control it?
Administrative: A shipping manager needs to determine how a new picking process will impact the movement of trucks within the distribution center. How would he know what factors to identify that would impact customer deliveries?

## Slide 3: Learning Objectives
To understand the concepts of the Failure Mode and Effects Analysis (FMEA) and its applicability to the evaluation of all processes.
To emphasize the importance of prioritizing process improvement opportunities.
Measure
Analyze
Improve
Control

## Slide 4: FMEA - Definition and Purpose
Definition-A structured approach to:
  identifying the ways in which a product or process can fail
  estimating the risk of specific causes with regard to these failures
  prioritizing the actions that should be taken to reduce the chance of Failure
  evaluating the design validation plan (Product) or the current control plan (Process) for preventing these failures from occurring
  Purpose
  Identify potential failure modes and rate the severity of their effects
  To rank order potential deficiencies
  To help focus on prevention
This tool is best used in a proactive manner, but may also be used in a reactive situation.

## Slide 5: Where do Risks Come From
Health, Safety
& Environmental
Market Pressures
Management Pressures
Technology
Development
Public Liability
Customer
Requirements
Warranty Services
Legal & Statutory
Requirements
Competition
Perceived Risks

## Slide 6: FMEA Benefits
General:
Improves the quality, reliability and safety of products and processes in a proactive manner.
Helps to increase customer satisfaction, by addressing failures that keep us from meeting critical customer requirements in processes or products.
Reduces product development timing and cost
Documents and tracks actions taken to reduce risk
Identifies potential process risks (e.g. HS&E, rework, late deliveries)

## Slide 7: When is an FMEA Started
Early in the process improvement investigation, after a process map has been developed.
When new systems, products and processes are being designed
When existing designs or processes are being changed
When carry-over designs are used in new applications
After system, product or process functions are defined, but before specific hardware is selected or released to manufacturing (ideally)
Did we think of Safety Concerns?

## Slide 8: When to Update an FMEA
Whenever a change is being considered to a product’s design, application, environment, material, or to a product's manufacturing or assembly processes.
On a regular basis:
  to review completion of action items
  recalculate RPN’s
  to develop actions and assign responsibilities to the new highest ranking RPNs.
The FMEA is a living document.

## Slide 9: FMEA Team
Team approach is necessary
The Black Belt leads the team
Recommended representatives (depending on project scope):
  Design
  Manufacturing Operators/Supervisors
  Quality
  Reliability
  Materials
  Testing
  Supplier
  Internal Customers (external where appropriate)

## Slide 10: Type of FMEA’s
System - used to analyze systems and sub-systems in the early concept and design stages. Focuses on potential failure modes associated with the functions of a system caused by the design.
Process - used to analyze manufacturing and assembly processes. Focuses on Process Inputs.
Design - used to analyze product designs before they are released to production. Focuses on Product Function.

## Slide 11: FMEA Thought Map
What is the Input
What can go wrong with the Input?
What is the Effect on the Outputs?
What are the Causes?
How Bad?
How Often?
How can this be found?
How well?
What can be done?

## Slide 12: Definition of Terms
Failure Mode - the way in which a specific process input fails - if not detected and either corrected or removed, will cause Effect to occur.
Can be associated with a defect (in discrete manufacturing) or a process input variable that goes outside of target range.
  Anything that an operator can see that’s wrong is considered a Failure Mode.
Effect - impact on customer requirements. Generally external customer focus, but can also include downstream processes.
Cause
  Sources of process variation that causes the Failure Mode to occur.
  Identification of Causes should start with Failure Modes associated with the highest severity ratings.
Current Controls
  systematized methods/devices in place to prevent or detect failure modes or Causes (before causing effects).
  Prevention consists of mistake-proofing, automated control and set-up verifications

## Slide 13: Linking Failure Modes to Effects
Failure Mode 1
Failure Mode 2
Effect 1
Failure Mode 1
Effect 1
Effect 2
Failure Mode 1
Failure Mode 2
Effect 1
Note that the relationship between the Failure Mode and the Effect is not always 1-to-1

## Slide 14: Risk Priority Number (RPN)
The output of an FMEA is the Risk Priority Number
The RPN is a calculated number based on information you provide regarding
  the potential failure modes,
  the effects, and
  the current ability of the process to detect the failures before reaching the customer
It is calculated as the product of three quantitative ratings, each one related to the effects, causes, and controls:
The Risk Priority Numbers are then sorted and actions are recommended for the top issues.
Effects
Causes
Controls
RPN = Severity X Occurrence X Detection

## Slide 15: Definition of RPN Terms
Severity (of Effect) - importance of effect on customer requirements - could also be concerned with safety and other risks if failure occurs (1=Not Severe, 10=Very Severe)
Occurrence (of Cause) - frequency with which a given Cause occurs and creates Failure Mode. Can sometimes refer to the frequency of a Failure Mode (1=Not Likely, 10=Very Likely)
Detection (capability of Current Controls) - ability of current control scheme to detect: the causes before creating failure mode and or the failure modes before causing effect (1=Likely to Detect, 10=Not Likely to Detect)
Rating scales should be developed by the team.

## Slide 16: FMEA Model

## Slide 17: Example Rating Scale
The 1, 4, 7, 10 scale is generally considered to be the best option.

## Slide 18: Dynamics of the RPN
Which ratings are most affected by design?
By manufacturing?

## Slide 19: General Steps in the FMEA
1. For each Process Input, list ways that it can vary or go wrong (Failure Modes)
2. Identify Effects associated with each Failure Mode
3. List all Causes for each Failure Mode
4. List the Current Controls for each Cause
5. Create Severity, Occurrence, and Detection rating scales
6. Assign Severity, Occurrence and Detection ratings to each Cause
7. Calculate the risk priority number for each potential Failure mode scenario
8. Determine recommended actions, with responsible parties assigned and estimated date of completion, to reduce High RPNs - Estimate effect of Actions on RPN (SEV, OCC, DET).
9. Take appropriate actions and re-calculate all RPNs

## Slide 20: FMEA Form - Initial Assessment

## Slide 21: FMEA Form - Long Term History

## Slide 22: Process Map to be Used in Example

## Slide 23: C&E Matrix Approach to FMEA
We will focus on the top priority items from the matrix for our FMEA:
  Scales Accuracy, DMF Load Accuracy, DMF Cleanliness and DICY Environmental Factors are the most important

## Slide 24: FMEA Form - Initial Assessment 1. For each input brainstorm what can vary or go wrong (Failure Modes) 2. Identify effects for each Failure Mode. 3. List potential causes for each Failure Mode. 4. List current controls. 5. Assign ratings based on agreed upon scale for severity, occurrence, and detection. 6. Calculate RPN by multiplication of severity, occurrence, and detection.

## Slide 25: Prioritization of Actions
Sort by RPN and fill in recommended actions only for top RPN’s
The key is FOCUS!

## Slide 26: FMEA Living Document
We have recorded when the action was taken and the impact on the RPN. The team rated Sev, Occ, and Det using the same scale developed previously. Notice that this is a nice way to track past activities.

## Slide 27: Approaches to FMEA’s
Approach One (C&E Matrix Focus)
  Start with Key Inputs with the highest scores from the C&E Matrix analysis
Approach Two (Focused):
  Fill out the Failure Mode and Effects columns of the worksheet. Copy to FMEA form and rate Severity.
  For High Severity Ratings, List Causes and rate Occurrence for each Cause
  For the highest Severity * Occurrence Ratings, evaluate Current Controls and develop actions for highest RPN’s
Approach Three (Comprehensive)
  Fill out the FMEA worksheet beginning with the first process step and ending with the last
Approach Four (Super Focused)
  Pick the top Pareto defect item (Fiber Breakouts) or Failure Mode (Variability in Temperature)
  Focus the FMEA process on only that defect or Failure Mode
  Purpose: To “Kill” that Failure Mode

## Slide 28
y=f(x)
Maps
Measurement Systems
Capability Analysis
  Histogram
  Control Chart
Fishbone Diagram
Cause and Effect Matrix
Failure Modes and Effects Analysis
Multi-Vari Studies
Design of Experiments (DOE)
DOE/ Evolutionary Operations
Control Plan
Statistical Process Control Charts
Analyze
Measure
Improve and Control
Process Improvement Plan Review

## Slide 29: Summary
We reviewed the importance of the FMEA
We discussed the link of the FMEA to the Process Map and C&E Matrix
We performed some exercises to complete an FMEA using the worksheet and the final FMEA form
The FMEA has been added as a tool to utilize in the prioritization of actions to go forward with on our search for understanding of our processes.

## Slide 30: Beyond Lean Online Resources

## Slide 31
www.BeyondLean.com
Thank You!