## Slide 1: Lean Six Sigma Certification & Training
Module 005 Section 003
Problem Solving

## Slide 2: Beyond Lean Online Resources
        Certification Courses and Exams
        Workbook Downloads
        Membership Online Training Videos
        LeanSigma Fast Action Implementation Guide
Order Support Products Here

## Slide 3
Where does Problem Solving
fit with Lean?
Notes: Problem Solving forms part of the Jidoka column of the Lean Temple
Jidoka roughly translated, means to stop as soon as an error has been detected. This can mean stopping a single task, or stopping an entire manufacturing line.
Once a problem has been highlighted it must then be resolved to prevent future disruptions to the flow of the standard work, the 6 steps approach is the ideal tool for these fast and effective solutions.

## Slide 4: Objectives
To have a structured method of investigating and resolving problems.
Understand the tools used and confirm the status of the task at each stage.
To deep dive into problems to ensure they are resolved 100%
Notes: The objectives are as follows:
To learn the basic tools and techniques to allow you to investigate and resolve problems effectivley.
To understand the various levels of problem solving

## Slide 5: Problem Solving - Definition
To truly solve a problem you must eliminate the root cause rather than manage the effects.
Notes: The root cause of a problem is the element which, when eliminated, will prevent the problem from ever occurring again.
Managing the problem means that a check / inspection or further work step has been put in place to prevent a problem from occurring. The difficulty with this type of approach is that if there is a chance the problem may occur again, then it probably will.

## Slide 6: Problem Solving - Why is it Important ?
Every problem solved eliminates waste and increases customer satisfaction.
Gives ownership of issues to the relevant parties
Creates a standard approach and therefore
cross-functional teams are easily assembled
Notes: Solving problems in a team environment is both useful for product and personal development.
Product development is improved directly from the problem solving process
Personal development comes from working with people who work in different parts of the business, such as purchasing, manufacturing engineering and design. Working with these people increases your business awareness and therefore grows the individual.
Customer satisfaction is also enhanced as their needs are being met with regard to cost, quality & delivery

## Slide 7: PDCA Problem Solving
P = Plan thoroughly
D = Do exactly as planned
C = Check accurately
A = Act accordingly and promptly
Notes: The PDCA approach to problem solving was first developed in the 1950’s by one of the most renowned quality gurus Dr. W. Edwards Deming.
Deming proved that his systems and techniques were effective in the United States during the second world war. The advantage that he had during this time was that of a new workforce, and one that had no pre-conceived ideas of how things should be done. This workforce consisted almost entirely of women, who were drafted in to work in industry whilst their men folk were off fighting in foreign lands.
Productivity soon exceeded that of pre-war America, with quality steadily rising to unprecedented levels.
Sadly the bubble burst when the men folk returned from war and resumed their occupations.
Deming frustrated, knowing that his techniques were no longer seen as a requirement in post war America went to help in the regeneration programme being undertaken by the allies in a small Pacific country devasted by the Americans use of Atomic weapons, which effectively ended the war.
The country of course was Japan and this man with new ideas was welcomed with open arms. He worked with companies such as Toyota, Nissan & Nippondenso.

## Slide 8: PDCA Problem Solving
When a proven solution is found the only method of sustaining that improvement is through Standardisation
Notes: Standards are not only the best method for sustainment but they are the foundation from which all improvements can be built and measured against.
Experience shows us that without standards their would be chaos:
Ask the team to think of standards by which we live:
Examples:
Moral Standards, Legal Standards, Engineering Standards, Education Standards, Food Hygiene Standards,
Trading Standards.

## Slide 9: The Structured Approach
Record the problem
Assign an owner
Form the best team for the problem
Use the best tools for the job
Record your results
Share the learning within the organisation
Notes: Record the problem on standard documentation which is the agreed format within the organisation.
Assigning an owner allows the problem resolution process to be managed.
Forming a team draws enables you to draw on a wealth of experience and knowledge
Using the best tools for the job, don,t use a sledgehammer to crack a walnut use a nutcracker
Recording your problems allows you to share your learning points with future groups and also for traceability
Shared learning within the organisation reduces the lead time to solve issues, it also makes people examine their current work processes, where they currently live with the type of problems that you have just resolved.
This type of shared learning activity is known as Jishuken

## Slide 10: Recording the Problem
Notes: A standard format adopted at FLS was the A/C Check Problem Resolution Board. This records the task reference card where the issue was identified, this information is only required however if relevant to the problem.
The nature of the problem is then recorded with any suggestions for resolution.
The Name of the person who raised the concern and if an aircraft mechanic their individual stamp
The date on which the problem was recorded.
The owner of the problem is then recorded after the weekly problem resolution meeting.
The action being taken is then recorded.
The next review date for that particular issue to be discussed
The overall status of the issue
1 Quadrant = No progress to date
2 Quadrant = Under Investigation
3 Quadrant = Plan Implemented and being monitored
4 Quadrant = Issue completed and will not re-occur

## Slide 11: 6 Steps to Problem Solving
Identify the most likely Probable Cause
Plan Containment
Plan Countermeasure
First impressions of Problem
Make the true problem clear
Identify the Location of the Problem Cause
Interrogate the Problem Cause
Analyse the Probable Cause
Uncover the Root Cause
Check
Implement Containment Action
Implement Countermeasure
P
D
C
A
1
2
3
4
5
6
Standardise the New Method
Notes: This diagram visually illustrates how a problem is reduced to the root cause before any planning can begin to first contain the problem and to then eliminate it completely using an effective countermeasure.
The diagram also shows how the PDCA improvement cycle is adopted.

## Slide 12: Problem Resolution Sheet
Each stage of the problem solving process is recorded using a standard sheet known as the “Problem Resolution Sheet”
Form a team
Clarify the problem & locate the “Cause”
Analyse the cause and identify the “Probable Cause”
Interrogate the probable cause to find the “Root Cause”
Put “Containment Action” in place
Brainstorm “Countermeasure”
Plan & implement “Countermeasure”
“Review Countermeasure” effectiveness
Notes: The problem resolution sheet is primarily a route map to problem solving, they should not be able to miss a stage of the process otherwise the end result “The Countermeasure” will be ineffective. It also allows the problem owner to visuall show the progress of the teams efforts at the weekly review meetings.

## Slide 13
Problem Resolution
Containment Action
3. Generate Ideas/Countermeasure
Sketch
x
Brainstorm
6. Evaluate the New Method
5. Implement the Plan Summary
4. Make an Improvement
Plan
Item
Resp
.
See Reverse of Sheet
2. Analyse the Current Situation
Clarify the problem
Locate Cause
Cause is:_____________________________
1. Analyse the Current Situation
1. Why
--
--------------------------------------
Because
2. Why
----------------------------------------
Because
3. Why
----------------------------------------
Because
4. Why
----------------------------------------
Because
5. Why
------------------
----------------------
Because
Root Cause is:___________________
Analyse the Probable Cause
5 Why’s
Analyse the Cause
Probable Cause is:__________________________
Item
Resp
Team
A
B
C
D
E
F
G
H
X
= easy to implement, not expensive
= requires planning and expenditure
=Too difficult, too expensive, long lead time
Problem Resolution Sheet
This document does not form part of aircraft documentation
Notes: Start the process at forming a team and follow the arrows through the process. Every area should be completed as what seems common sense at the time of working through the problem is not always so clear later on.
Remember these documents are to be shared with other people in the group disconnected from the process.

## Slide 14: First Impression of Problem
Most people, when faced with a reported problem for the first time, tend to do the following:
Listen to hearsay about problems
Make assumptions about the likely causes
This distorts the real truth and problems appear larger than they really are.
Remember this simple saying next time you are faced with a problem.
To ASSUME is to make an ASS of U and ME

## Slide 15: Step 1. Problem Cause
There are two basic methods of clarification, and both have their own place as to when they should be used
  Pareto Analysis – best used where sufficient data is already available or can be collected quickly.
  Process Flow Maps – Identifies the sequence of events that should occur to produce a quality product or process. Using basic elimination techniques the Problem Cause can easily be identified

## Slide 16: Identifying the Cause
Correct component delivered
Correct component ordered
Correct component fitted
This is the problem cause as the first in a chain of events to be wrongly executed
Each entry should be written as if task completed correctly e.g.: Correct component fitted rather than wrong component fitted
Notes: Flow charting is a very basic technique, but is makes the team think at the process level, it is sometimes best to write the flow chart onto a flip chart or white board whilst you try to establish the critical areas of the flow. When you are decided that this has been achieved you should then transfer the three most critical stages onto the six steps problem solving worksheet.
Each entry on the basic flow chart should be written as though the task was executed correctly.
The reason for this is that we determine, as a team whether or not the task was carried out correctly and tick or cross depending on the answer. We are looking for any X’s to appear to show that a task has been incorrectly executed.
For example if we wrote in a box “incorrect component fitted”, and this was actually the case, we would tick the box rather than placing an X to show that the task was carried out incorrectly.

## Slide 17: Step 2. Identify the Probable Cause
Once we have found the cause, this must then be interrogated to establish the Probable Cause.
This is best done using a structured brainstorming tool known as the Cause & Effect Diagram.

## Slide 18: The Cause & Effect Diagram
PROBABLE CAUSE
MANPOWER
MACHINERY
METHOD
MATERIALS
Notes: The cause & effect diagram guides people into four main topic areas.
Manpower – this can cover areas such as training, manpower planning issues
Machinery – Equipment failure, wrong equipment, not enough equipment etc
Method – No standard approach, wrong method,
Materials – Wrong materials, no materials available, no material ordered

## Slide 19: Golden Rules of Brainstorming
No ideas should be mocked
Nobody should be refused a turn
Every suggestion offered should be recorded
Notes: Failure to obey these rules could stifle an individual whom might have more to offer the process.
Each idea is then written onto one of the small bones leading from one of the relevant four M’s of the cause & effect diagram.

## Slide 20: The Cause & Effect Diagram
PROBABLE CAUSE
MANPOWER
MACHINERY
METHOD
MATERIALS
Training
Poor Reliability
No standard Approach
Poor manpower allocation
New ideas not listened to
Wrong parts delivered
Shortages
No Spares
Notes: The cause & effect diagram is also known as the fishbone diagram due to its general shape, it is also known as the Ishikawa diagram. This is after the techniques inventor Kaoru Ishikawa who is regarded as the leading contributor to Japanese quality management.
As you can see from the above example, ideas that have been brainstormed are placed under the appropriate heading, this is usually carried out by one member of the team whilst the remaining members call out their ideas in turn.
The beauty of the Ishikawa diagram is that it fits with the visual management philosophy of being able to understand the issue within 3 minutes. “3 Minute Management”

## Slide 21: Nominal Group Technique
Unless the Probable Cause is consensed by the group, you may take the wrong path with subsequent problem solving activities.
This can happen quite easily if there is a dominant team member.
The emotion can be removed from the process using, The Nominal Group Technique.

## Slide 22: Nominal Group Technique - cont
Make a simple graph & take the 5 most likely ideas
Grade each from 1=Least Likely - 5=Most Likely
Then total the scores for the 5 ideas
A consensus of opinion can now be drawn

## Slide 23: Nominal Group Matrix
Idea
Sean
Name
Idea A
Idea B
Idea C
Idea D
Idea E
Paul
1
2
3
4
5
5
2
1
4
3
Thomas
2
1
4
3
5
John
1
2
3
5
4
Piers
2
3
1
4
5
Total
11
10
12
20
22
Note: If Sean had been a powerful member of the group he could have persuaded the team to waste time addressing Idea - A
Notes: Using the nominal group technique removes emotion from the process. The matrix should also be recorded, this is a requirement should the idea consensed be wrong, then the next most likely cause can be used without the entire process being conducted again.

## Slide 24: Step 3. Root Cause Investigation
The Root Cause is the key element of the problem, which when resolved will prevent re-occurrence
The tool used to identify the Root Cause is the
“5 Whys”
Notes: The Root Cause investigation is the final stage in defining the problem, only when the root cause has been identified can you begin to solve the problem.
Most people when problem solving reach the probable cause and then begin to try and resolve the issue. This usually results in the effects of the problem being minimised but never resolved.
The main issue with minimising the problem is that extra resource and time are used where as, resolving the root cause there may be an initial, but no long term impact upon these areas.

## Slide 25: The 5 Whys
In theory this appears to be the simplest of techniques, but in practice it is significantly harder than anything else you will encounter in the problem solving process.
The aim is to ask why of the Direct Cause and then to ask why of the subsequent answers until the question why has been asked an average of 5 times.
Notes: The key to the 5 whys technique, is for the group to stay within the bounds of which they are able to control.
Areas which cannot be controlled are topics such as human behaviour, senior managements methods, changing the past etc.
If the answers to the question why are straying in this direction you must reign the team back and focus on those areas which they can control.

## Slide 26
<number>
Why is there insufficient oil?
 “Oil pump not working”
Why is the oil pump not working?
 “the filter is blocked with swarf ”
Why is the filter blocked ?
 “there is no cleaning procedure”
The ‘5 Whys’
Why has the machine stopped?
 “fuse has blown”
 “A lack of oil on the drive shaft”
Why did the fuse blow?
Notes: Slide number <number>

## Slide 27: Step 4. Containment Action
Once the Root Cause has been identified, a short term solution is required.
This is known as a containment action and will alleviate the immediate concern.
Traditionally this type of solution becomes the long term fix eliminating the customer concern. The waste however of rework or over processing remains within the organisation.
Notes: The containment action is a way of preventing the problem rather than curing it. This type of action relies heavily on techniques such as additional processing built in to the standard tasks which increase the operator burden, or 100% inspection and rectification.
None of these methods should ever be accepted as the solution to a problem.
The containment action is also an excellent tool for confirming that the countermeasure put in place has been successful.
By removing the containment after the countermeasure has been running for a few days, you are confirming the effectiveness of the countermeasure.

## Slide 28: Step 5. Countermeasure
A Countermeasure or elimination of the Root Cause is now required.This can be achieved using tools illustrated earlier.
Solution & Effect Diagrams (Reversal of Cause & Effect)
Brainstorming
Nominal Group Technique
Notes: Countermeasures should improve a process by eliminating a problem and without adding any non-value added elements to a process.

## Slide 29: Step 5. Countermeasure - cont
Once you have decided upon the best agreed countermeasure, you will need to plan its implementation.
The planning stage is very important to you as the owner so that you are able to carry out the following.
Notes: Proper planning and preparation are all important to enable the countermeasure to be successful.
All members of the team should be involved with the planning stage. Everybody should be in agreement that the required actions to execute the plan successfully are correct.

## Slide 30: Step 5. Countermeasure - cont
Regularly review progress of the projects vs. the plan
Assign ownership to those involved
Report back accurately regarding the status
Support those areas where slippage is occurring
Save information to use as a reference for similar issues in the future

## Slide 31: Step 5. Countermeasure - Plan
1. Containment Action in place
2. Resource allocation for project
3. Planning what the countermeasure will look like
4. Making of the countermeasure
5. Training those involved in using the countermeasure
6. The implementation date
7. Status Review Meetings
Owner
Action
Date
Wk1
Wk2
Wk3
Wk4
Wk5
No
The above 7 actions should always be included as part of the implementation plan
Notes: Containment action in place – Without this action the problem will continue until the countermeasure is in place and working effectively
Resource allocation for project – Without people the plan is useless, without parts and tooling the plan is useless
Planning what the countermeasure will look like – This can mean designing a poka-yoke device to planning a layout change & standard work
Making or Implementing the Countermeasure – How long will it take & who will make, move or write it
Training those involved with the use of the countermeasure – Quite often changes can be made to a working environment or process without operators knowledge. This creates resistance immediately to the new changes and however good they could fail without operator support. Therefore communication at each stage and end user training are crucial to the success of all changes no matter how small.
The implementation date is key as this drives the team to meet their objective
The implementation date is symbolised using a diamond. This symbol is also used for key events within the plan.
Status review meetings – These meetings are their to ensure that no task can slip further than one review. Therefore the fewer reviews which are scheduled into the plan the less control the owner of the plan has.
The review dates are symbolised using an inverted triangle

## Slide 32: Step 5. Countermeasure – Plan Review
1. Containment Action in place
2. Resource allocation for project
3. Planning what the countermeasure will look like
4. Making of the countermeasure
5. Training those involved in using the countermeasure
6. The implementation date
7. Status Review Meetings
Owner
Action
Date
Wk1
Wk2
Wk3
Wk4
Wk5
No
Illustrates Behind Schedule
Illustrates Ahead of Schedule
Illustrates on Schedule
Notes: The red lines depicted on the plan are project status lines. They are a simple visual method of determining who is ahead, behind, or on target with their area of the plan.
This technique is used to draw attention quickly to those areas requiring support and to minimise the amount of detailed explanations required at meetings. These lengthy explanations can destroy meetings as people tend to switch off.

## Slide 33: Step 6. Review Countermeasure
Develop a plan to Check that the countermeasure has worked. The best method of doing this is to remove the containment action.
Use the same method as previously illustrated to check and review the status of the countermeasure
Measure the following:
Key performance indicators (Is the process/product repeat ably to the required standard)
New effects (Have the processes you have introduced caused any new issues)
Notes: Key performance indicators – these can be quality measures using pareto analysis or spc charts
Other types of key performance indicators can be on time delivery, planned production versus actual etc.
New effects – Has there been any effects created by the changes implemented, these may not always show on the KPI’s. Interviewing people within the process and also the internal process customers & suppliers can usually be the most effective method of tracing these issues.

## Slide 34: Step 6. Standardise Countermeasure
Once the team is happy that the countermeasure is successful they then need to standardise it.
This can be done using several methods from placing on daily checklists or writing a formal procedure to implementing a mechanical method company wide on all like processes
Daily Checklists
Formal Procedures
Mechanical Method
Notes: Standardisation of a countermeasure prevents the progress made from slipping back to the original condition. The standardisation can take many different forms from a simple written standard in which everybody is trained to a standard error proofing device which will automatically prevent or highlight defects as they occur. These types of error proofing devices are known as Poka-Yoke devices.

## Slide 35
www.BeyondLean.com
Thank You!