## Slide 1: Lean Six Sigma Certification & Training
Module 003 Section 004
Standardised Work Overview

## Slide 2
Standardised Work Overview & Documents
Notes: <number>
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 3: Standard Operations
Definition
Best combination of worker and machine to achieve output with minimum labour, space, inventory and equipment.
Objectives
To establish and clarify the guidelines for manufacturing Quality, Quantity, Manpower, Inventory, and Safety
Provides a tool for Kaizen
Where there is no standard there can be no KAIZEN
Notes: <number>

## Slide 4: Standard Operations
Takt time/ Cycle time
Work sequence
Standard WIP
Notes: <number>

## Slide 5
Takt Time
Takt is a German word
It is the principal that all activity within a business is
sychronised by a pulse, set by the customer
demand
It describes the conductors
baton
Notes: <number>
(READ SLIDE)

## Slide 6
Takt time relates the customer demand to the time available.
Takt = Production Time Available
Customer Demand
Time is deducted for:
Lunch and tea breaks
Team briefing times
TPM breaks
Clean down time
E.g 8hrs x 60 = 480 minutes
Time Available = 480 – 20 mins breaks – 10 mins TPM
= 450mins
How To Calculate Takt Time
Notes: <number>
Talk through the differences between these concepts briefly
Explain that we may set our target cycle time faster than Takt in order that we can stop production in the event of a problem without immediately effecting the customer delivery.
The principal of Autonomation states that the process should halt when an abnormality occurs. In order to enable this, we must be able to halt production without immediately impacting on the customer requirements.
OPR should be increased as the processes become more capable.
A typical OPR at the last stage of a process might be 90%
Target Cycle Time = Takt Time x OPR
Where OPR = Operation Performance Rate
e.g if a line has an OPR of 95% due to problems, the target cycle time would be
Target Cycle Time = Takt x 0.95

## Slide 7
If the customer demand is 500 units per week;
Demand = 500 / 5
= 100 products a day
Takt Time = Time Available
Customer Demand
= 450 mins
100
= 4.5 mins or 270 secs
How To Calculate Takt Time
Notes: <number>

## Slide 8
Takt, Cycle, Target Cycle and Lead Time
Takt Time = The pace at which the customer requires products
Target Cycle Time = The pace at which we will produce to ensure we meet the customer requirements
Cycle Time = The time at which a process cycles
Lead Time = The total production lead time from product start to finish
Don’t get them confused!!
Notes: <number>
Talk through the differences between these concepts briefly
Explain that we may set our target cycle time faster than Takt in order that we can stop production in the event of a problem without immediately effecting the customer delivery.
The principal of Autonomation states that the process should halt when an abnormality occurs. In order to enable this, we must be able to halt production without immediately impacting on the customer requirements.
OPR should be increased as the processes become more capable.
A typical OPR at the last stage of a process might be 90%
Target Cycle Time = Takt Time x OPR
Where OPR = Operation Performance Rate
e.g if a line has an OPR of 95% due to problems, the target cycle time would be
Target Cycle Time = Takt x 0.95

## Slide 9: Standard Operations
Operator Cycle time
The total time required for a worker to complete one cycle of an operation. Includes manual operations, walking, inspecting, unloading/ loading machines, gauging.
Does not include waiting for machine auto cycle to finish
Machine cycle time
The total time for a machine to finish one complete machining cycle, including loading and unloading time
Cycle times must be separated between work done by a machine without human involvement and work that requires humans and machines working together.
Notes: <number>

## Slide 10: Work Sequence
  Sequence of activities that each worker performs to complete one cycle
  Does not necessarily represent the part routing
  Requires multi-skilled workers
F.G.
I
H
G
F
E
D
C
B
A
R.M.
6
1
2
3
4
5
5
1
2
3
4
Notes: <number>

## Slide 11: Standard in Process Stock
Specified minimum number of pieces of inventory required to conduct the work sequence in demand
  Automatic operations require standard in process stock to enable the worker to separated from the automatic cycle
  No standard in process stock is required at manual operations
Notes: <number>

## Slide 12: Standard in Process stock
C
D
E
F.G.
R.M.
B
A
C
D
E
F.G.
R.M.
B
A
All manual operations:
SIPS = 0
All automatic operations:
SIPS = 5
Notes: <number>

## Slide 13: Lean Manufacturing
Tools for Standard Operations
Notes: <number>

## Slide 14: Tools for Standard Operations and Kaizen
Time observation forms
  To observe the operations and break into elements
  To establish best/ repeatable elapsed time per element
  Process capacity table
  To determine if machines have enough capacity
  To determine the level of man power in the cell
  Standard work combination sheets
  To determine best combination of worker/ machine
  One SWCS/ operator- posted in the cell
  Standard work layout
  To train new operators
  To record actual layout and flow
  One SWL/ operator- posted in the cell
  Work Instruction Sheet
  To train new operators
  To standardise the “knack”
Notes: <number>

## Slide 15: Standard Work Documents
Order in which the documentation should be used:
Process Capacity Table
Calculate Takt Time
Standard Work Layout
Standard Work Combination Sheet
Standard Operating Procedure
Work Instruction Sheet
Notes: <number>
Read from the slide:
in some instances we may need to start at different levels due to business needs or model line maaturity.

## Slide 16
Notes: <number>
This document is used to collect data on cycle times. Once the data is collected the cycle time chosen to standardise is the best repeatable time. If we go for the shortest time we may uncover problems such as: work being missed, short cuts or that somebody just does it differently than everybody else. If we go for the longest time then this will not give us a true representation of what is actually happening as this may show that the operator has gone to the toilet or coffee or for a fag etc.

## Slide 17
Notes: <number>
Explain the document and why we use it.

## Slide 18: Process Capacity Table Calculations
Total capacity =
Machine cycle time = Manual time and Automatic time
Machine Cycle Time per piece =
Quality Check Time Per Piece =
Inspect Time per piece
Frequency of check
Time to set up
Number of pieces per set up
Net operating time
(Mach. Cycle time + Toolset up Time per Piece + Quality Check per Piece
Notes: <number>
Read through the calculations.

## Slide 19
Notes: <number>

## Slide 20: Process Capacity Table Example
Exercise 1
OPERATOR
CYCLE
TIME
AUTO
CYCLE
TIME
NO. PIECES
PER CHANGE
TIME TO
CHANGE
(SECONDS)
(SECONDS)
(MINUTES)
ROUTING
LATHE
GRINDING
SLOT KEYWAYS
INSPECT
OTHER
6
6
5
7
26
30
18
200
50
100
50
10
60
All walk times between operations = 2 seconds
Pick up RM & put down FG = 2 seconds each
Net operating time = 460 minutes / shift
One shift operation
Customer demand = 690 pieces / shift
Notes: <number>

## Slide 21
Notes: <number>

## Slide 22: Process Capacity Table
Clearly there is a bottle-neck situation, action needs to be taken to
ensure that the customer is supplied with the required parts
There needs to be a 2 point action plan ;
Short term - run the relevant processes through lunch breaks and use overtime
Medium term - machine base kaizen to reduce the process time to ensure demand is met
Notes: <number>

## Slide 23: Process Capacity Table
When all the capacities have been calculated it is vital to identify the “bottle-necks” within the cell.
The bottle-neck process is any process within the cell that is not able to produce to the customers requirement
This means that if any figure in the “capacity” column is less than or equal to the maximum output per day figure, then this is a BOTTLE-NECK PROCESS
Notes: <number>

## Slide 24: Standard Work Documents
STANDARD WORK COMBINATION SHEET
The standardised work combination table is a simple graphical based picture showing the work sequence for a worker and the times to complete each process
The purpose of the chart is to :-
Identify the work sequence for the worker
Identify the time for each element that they are doing
Act as a foundation for Kaizen
Notes: <number>

## Slide 25: Standard Work Documents
STANDARD WORK COMBINATION SHEET
In order to complete the Standard Work Combination Chart, we therefore need to know which operations will be carried out by which worker.
This is done through work balance
Notes: <number>

## Slide 26
Notes: <number>

## Slide 27: Standard Work Documents
STANDARD WORK COMBINATION SHEET
Manual work is shown as a solid line
Automatic processing is shown by a dotted line
Walking time is shown by a wavy line
TAKT TIME is shown by a vertical RED line from top to
The bottom of the graph (write TT in red at the top of the line)
If any waiting time occurs indicate by using double ended arrows
Notes: <number>

## Slide 28: Standard Work Documents
If the total manual cycle is shorter than TAKT time use the
waiting symbol to show the gap between when
the cycle finishes and the red TAKT line.
Notes: <number>

## Slide 29: Standard Work Documents
If the situation occurs where the total Manual Cycle Time
Is greater than the TAKT time, the following actions must happen:
Short term - put in extra manning to reduce the Total Manual
Time to below TAKT TIME
Medium Term – Kaizen the process to reduce the Total Manual
Time below TAKT TIME
Notes: <number>

## Slide 30: Standard Work Documents
Standard work layout
This a very concise document designed to give a pictorial view of the production process (cell/ Jig). The purpose of this document is:
Identify the physical shop-floor layout of the cell
Identify which processes need quality checks and where they occur
Identify where any safety precautions are
Identify where and how many standard in process stock are required to run the process
Notes: <number>

## Slide 33: Time Observations After Kaizen
PRODUCT:
Times below are in seconds
Routing
Saw
Drill
Degrease
Weld
PU & PD for heat treat
Treat
Turn
Grind
Gun drill
Inspect
Pack
Other
All work time = 2 seconds between operations
Pick up (PU) raw material = 1 second
Put down (PU) finished goods = 1 second
Net operating time = 456 minutes per shift
(2 x 10 minute breaks + 4 minute clean up)
Requirements = 380 units per shift
Welded piston
Manual
Automatic
Total
8 9 17
8 34 42
7 7
7 14 21
2
2
12 16 28
8 13 21
11 22 33
18 18
30 30
Exercise 1
Determine:
Takt time & manning requirements
Standard work layout
Standard work combination sheet
Notes: <number>

## Slide 34: New Layout for Example 1
INSP
RM
FG
S
A
W
DRILL
D
E
G
WELD
TURN
GRIND
GUN
DRILL
PACK
HEATTREAT
TO AND FROM
HEAT TREAT
Notes: <number>

## Slide 35
New Layout for Example 1
INSP
RM
FG
S
A
W
DRILL
D
E
G
WELD
TURN
GRIND
GUN
DRILL
PACK
HEATTREAT
TO AND FROM
HEAT TREAT
68
69
SECONDS
SECONDS
1
8
8
8
1
7
7
2
12
18
30
11

## Slide 38
Notes: <number>

## Slide 39
www.BeyondLean.com
Thank You!