## Slide 1: Lean Six Sigma Certification & Training
Module 005 Section 004
Line Balance – Yellow Belt

## Slide 2: Beyond Lean Online Resources
        Certification Courses and Exams
        Workbook Downloads
        Membership Online Training Videos
        LeanSigma Fast Action Implementation Guide
www.lean-six-sigma-certification.com

## Slide 3: Introduction : What is line balancing?
Everyone is doing the same amount of work
Doing the same amount of work to customer requirement
No one overburdened
No one waiting
Everyone working together in a BALANCED fashion
Variation is ‘smoothed’
Notes: <number>
Ask the audience what they know about line balancing
Jot down their answers on a flip chart
When you have exhausted the responses go through this slide (the points will appear one at a time)
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 4
Example : Line Balance Chart
This is a VISUAL production tool that enables the planning and organisation of individual, TIMED items of work to create the foundation for a balanced production line.
It is used as a tool to continuously drive out waste from operations and processes and it is also a valuable tool in implementing changes in customer demand,
Notes: <number>
This is an example of a line balance chart
The Line balancing board is a management tool that visually represents the elements of standardised work in a clear and easy to understand way.
The line balance chart serves many purposes ranging from being a very simple “snapshot\layout” of a process to a much more detailed planning and organisation tool . However all it’s functions are used in conjunction with setting up and maintaining manufacturing processes
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 5: Line Balance : Simple Example
1
2
3
4
25 mins
5 mins
15 mins
10 mins
Constraint
Overburden
This operator must WAIT for operator 2
Overproduction which causes the other 6 wastes
Waiting
Over-processing
Inventory
Rework
Transportation
Motion
This operator must WAIT for operator 3
5
10
15
20
25
1
2
3
4
mins
Notes: <number>
This is a simple example.
Here we have four processes, each with different process times (depicted below in graph form).
As you can see, operation 1 has the shortest time and operator 2 has the longest. Therefore, operator 2 is the CONSTRAINT.
This means that operator 2 will have to do more work than the others meaning that he is OVERBURDENED. Since operator 1 has the shortest time it means that either he sits and WAITS for operator 2 or he OVERPRODUCES to fill his time. This creates the INVENTORY that you can see.
The other following operations tend to WAIT for Operator 2 also.
If Operator 1 does OVERPRODUCE, then this tends to create the other WASTES in the system. The wastes can be identified into 7 categories…..
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 6: Line Balance : Simple Example
5
10
15
20
25
Redistribute the work
1
2
3
4
15 mins
15 mins
15 mins
10 mins
Promotes one-piece FLOW
Avoids overburden
Minimises the 7 wastes
Reduces Variation
Notes: <number>
If we were to re-allocate some of the work from operator 2 onto lets say operator 2 then we can see how this can make the line more BALANCED.
This reduces VARIATION in the process,
Minimises the 7 wastes
Avoids overburden
And promotes one-piece-flow.
Once again , all of these attributes help achieve a stable work environment in which variations can be detected quickly and dealt with. The customer or final in-process-stock also receives a consistent supply of product.
Due to the low level of inventory in the system, if the customer changes his order drastically the system allows you to be flexible as you do not have to scrap large amounts of stock.
Rather than working in batches, this system also encourages you to change over more frequently. At first this may be an issue as the process may not be set up for this. However, this is where change over reduction activities can be used
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 7: Pre-requisites to line balancing…
Standardise
Calculate Takt
Achieve CONSISTENCY in operations
Enabling us to achieve our customers requirements by ‘managing our production effectively’
Variation in our operations demands more human intervention which, increases the risk of HUMAN ERROR
Understand the ‘drumbeat’ of the CUSTOMER
Notes: <number>
These are the two pre-requisites to line balancing.
Takt time is simply the ‘time available to produce components in a year’ divided by the ‘customer demand’ giving you a drum beat of customer demand.
I f we know how many products we need to produce at regular intervals then we can balance production to meet this. Ensuring that we always meet our customer requirements.
It also enables us to calculate the required level of manning for production also.
STANDARDISE – what we mean by this is STANDARDISING the operations so that we have a base line on how the job should be completed. This enables better management of the process and problems or variation from the process can be determined more effectively. This is vitally important as one-piece-flow demands that you are able to resolve issues quickly. Otherwise you will stop the customer ultimately!!
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 8
Takt Time
Takt is a German word
It is the principle that all activity within a business is
synchronised by a pulse, set by the customer
demand
It describes the metronome
Takt = total time available*
total customer demand
Notes: <number>
(READ SLIDE)

## Slide 9
Customer demand = 10 units / month
Total time available = 20 days
Drumbeat = 1 part every 2 days
Each process needs to complete one unit every 2 days
Process 1
Process 2
Process 3
Customer
Every 2
days
Process 4
Process 5
Takt time
Takt = total time available
total customer demand
Every 2
days
Every 2
days
Every 2
days
Every 2
days
Notes: <number>
If you were required to produce 10 units a month, then a in a 20 day month you would simply need to produce 1 unit every 2 days.
This also enables you to visually manage your production more effectively. If you know that you are to produce a component every two days then you know that after 1 day you should have completed 50% of that component, and at lunch time you should be 25% of the way into completing the first part. If for any reason this is not the case then production management need to understand why that is the case and react accordingly (using problem solving techniques and escalating the issue if necessary).
Visibly displaying this situation enables management to closely manage production more effectively. This enables adherence to TAKT (customer requirement) and makes sure that issues are resolved as they occur. In this way the issues that occurred frequently in the past will gradually decline in there occurence creating a more stable environment.
In this stable environment people can spend more time focusing on continuous improvement of the process and resource can be freed up for other activities.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 10: Standardise
Highlight key information
Capture the layout
Indicate how the work flows
Notes: <number>
Standard formats are popular tools for detailing the way that process should be run or managed.
Here is an example of a ‘Standard work layout’ document which would be used to detail:
How the cell should be layed out (position of machines/ people / Stock locations
How the material should flow through the area.
Highlighting Health and safety information.
This document should be signed off by the team leaders of the area and the local area manager. It should be visibly displayed in the area for all to see (along with other standard documents or on a visual management board.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 11: Standardise
Notes: <number>
This standard is really the ‘manufacturing way’
If the process is detailed in this way and worked to then the process becomes more manageable and is a ‘stake in the ground’ for improvements to made
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 12
The benefits of the pre-requisites
Takt time
Standard Operations
What do you think are the benefits?
Notes: <number>
Ask the audience why THEY think TAKT and STANDARD OPERATIONS are important pre-requisites.
Jot their answers on a flip chart
Discuss their responses (10 minutes)
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 13
Takt time maximises the productivity due to:
Easily managed processes
Output of each process matches customer demand
Standard Operations provide:
Capable and repeatable processes
Process control at source
Improves accuracy of planning
Better adherence to plans
A platform from which continuous improvement can be made
Reduced costs
Improved quality
Basis for training
The benefits of the pre-requisites
Notes: <number>
If the audience has not been able to come up with all of the answers then read through this slide as a back up.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 14
www.BeyondLean.com
Thank You!