## Slide 1: Lean Six Sigma Certification & Training
Module 006 Section 004
Takt Time

## Slide 2
Which of these is Important to Our business?
Satisfied Customers
Profit
Growth
Market Share
Effective use of its people and plant
Maximum Capacity Production
Notes: <number>
Which of these are important to our business?
(Ask the question of the delegates for each statement, clicking the mouse will reveal the tick or cross one at a time)
(Once the ticks are revealed, prompt discussion as to why these are important to the company)
(The group will most likely answer ‘yes’ to the maximum capacity production. Reveal the cross, but don’t explain why at this stage.)

## Slide 3: Why Not Maximum Capacity?
Producing more than the customer requires is:
This is the greatest of the Seven Wastes
As it leads to occurrence of the other six
OVER-PRODUCTION
Notes: <number>
‘Maximum Capacity Production’ is not what we want for our company because it is producing more than the customer requires at any one period.
This is Over-Production, as we have just seen, one of the 7 wastes.
Over-Production is the greatest of the 7 wastes as it incurs the other six.
Why might we produce at full capacity regardless of the customer requirement?
E.g. to cover breakdowns, shortages, absence, scrap produced etc.

## Slide 4: The Western Approach
We produce more than we require to allow for problems
This embeds waste in our business
1
2
3
Notes: <number>
Throughout a production stream, each operation will conventionally produce regardless of previous or following operations.
The isolated environment that the division of labour has created under Western production systems gives little or no links between process operations.
Each operation produces as much as it can and then ‘pushes’ it on to the next stage.
THIS EMBEDS WASTE IN OUR BUSINESS

## Slide 5
‘Push’ Production System
Customer
If we consider production operations as a chain…
Each link producing in isolation at
full speed will cause a mismatch between links
Some areas over-produce, some cannot keep up...
?
Notes: <number>
Each link in the chain is the output of a process operation.
The customer wants the complete chain, one of each link joined together.
(Clicking the mouse will reveal what mismatches between operations may incur.)
(Point out that some operations have over-produced their link, some have not produced anything.)
The customer does not have any finished product, but there has been resource spent on producing.

## Slide 6: ‘Push’ Production System
Customer
What will happen when a link in the chain breaks
Within a ‘Push’ System?
Notes: <number>
(CLICK to reveal the chain)
(Describe the Value chain of a product, CLICK with the customer at the end.)
CLICK
The arrows represent the ‘Push’ of material / product from one operation to the next.
CLICK
(Ask the question of the delegates and discuss responses before showing next slide.)

## Slide 7: ‘Push’ Production System
Customer
The individual links keep building to schedule and…
The chain soon backs up
Notes: <number>
(Reveal the slide and prompt discussion.)
The operations preceding the break in the chain continue to produce, and the build up that is created from this causes a backlog.
The break in the chain may also be caused by the operation taking longer to complete, I.e a bottleneck
(Ask if the delegates can offer any experience of a situation related to this concept.)

## Slide 8: ‘Push’ Production System
Customer
When we consider the wider system…
We see why stock is present.
To buffer the unevenness of work
To buffer the breaks in the chain
STOCK / WIP
Notes: <number>
We can relate this model to a wider system, the breaks that regularly occur and the build ups that they cause.
CLICK
What do the red circles represent that we physically see every day in our production facility?
CLICK
The red circles identify the Stock / WIP
The isolated nature in which the links operate necessitate Stock / WIP between the links of the chain, to buffer the breaks.
CLICK
So we see why stock is present.

## Slide 9
Just In Time
The Just in Time branch of the
Lean Production System
is constructed of four key
elements
Notes: <number>
The Just in Time Philosophy comprises 4 elements.
Takt time is the driver of Just In Time. It is the pulse of the production system.
Without Takt time, the others are not possible.

## Slide 10
Takt Time
Takt is a German word
It is the principal that all activity within a business is
synchronised by a pulse, set by the customer
demand
It describes the conductors
baton
Notes: <number>
(READ SLIDE)

## Slide 11
Takt Time determines;
The pulse of the Production System
Pace of sales
Links production activity to actual customer demand
Ensures all production activity will be synchronised
from 1st process to final assembly process. - FLOW
Notes: <number>
Takt time is geared to the pace of sales.
A flexible organisation must respond rapidly and efficiently to changes in customer demand. Markets are changing constantly. Scheduling and forecasting tools are fundamentally flawed because we can never anticipate 100% accurately the shifts in Market demand. Thus scheduled production based on forecasts produces inaccuracies that are buffered by inefficiency in our business.
Takt time links the pace of sales with production, mandating that a production system is flexible and linked to actual customer demand.
Takt time is used to ensure that all operations and processes are synchronised to the same drum beat. Operations in our production chain can then be ‘tied together’ by introducing other elements of Just In Time.

## Slide 12
Takt time relates the customer demand to the time available.
Takt = Production Time Available
Customer Demand
Time is deducted for:
Lunch and tea breaks
Team briefing times
TPM breaks
Clean down time
E.g 8hrs x 60 = 480 minutes
Time Available = 480 – 20 mins breaks – 10 mins TPM
= 450mins
How To Calculate Takt Time
Notes: <number>

## Slide 13
If the customer demand is 500 units per week;
Demand = 500 / 5
= 100 products a day
Takt Time = Time Available
Customer Demand
= 450 mins
100
= 4.5 mins or 270 secs
How To Calculate Takt Time
Notes: <number>

## Slide 14
Takt, Cycle, Target Cycle and Lead Time
Takt Time = The pace at which the customer requires products
Target Cycle Time = The pace at which we will produce to ensure we meet the customer requirements
Cycle Time = The time at which a process cycles
Lead Time = The total production lead time from product start to finish
Don’t get them confused!!
Notes: <number>
Talk through the differences between these concepts briefly
Explain that we may set our target cycle time faster than Takt in order that we can stop production in the event of a problem without immediately effecting the customer delivery.
The principal of Autonomation states that the process should halt when an abnormality occurs. In order to enable this, we must be able to halt production without immediately impacting on the customer requirements.
OPR should be increased as the processes become more capable.
A typical OPR at the last stage of a process might be 90%
Target Cycle Time = Takt Time x OPR
Where OPR = Operation Performance Rate
e.g if a line has an OPR of 95% due to problems, the target cycle time would be
Target Cycle Time = Takt x 0.95

## Slide 15
Takt, Cycle, Target Cycle and Lead Time
Takt Time
Target Cycle
Time
Cycle
Time
+
+
+
+
+
=
Lead
Time
Notes: <number>
Show how these different time concepts are visible from a line balance board

## Slide 16
Flow Production
Customer
The customer takes a product from the end
Of the chain
Each link in the chain takes from the previous link
And processes produce to fill the gap that has been
created
What will happen when a link in the chain breaks
Notes: <number>
We have already considered our production chain within a typical western ‘Push’ manufacturing system.
We saw what effect breaks in the chain have on the overall system and the inherent waste that we incur in buffering these breaks in the production chain.
Now we will model a ‘Pull’ system in the same manner;
CLICK
Our chain is the same, CLICK, our customer is the same.
CLICK
In a pull system, work is ‘Pulled’ along the chain as it is needed by the customer.
Each operation, starting with the link closest to the customer, then pulls from the previous operation, creating a gap along the chain. The operations then produce to fill this gap.
(Ask question of delegates)

## Slide 17
Customer
Flow Production
If a link in the chain breaks...
The chain stops.
If the Customer does not pull from the end...
The chain stops.
Notes: <number>
(REVEAL SLIDE)
Delegates ,may point out that in this environment we would never build an aircraft if production stopped for every little break in the chain.
(Show next slide)

## Slide 18
Takt Time, an enabler for Flow
If work balance is set to Takt, the process closest the
customer can pull production through the system at
the right pace. This includes material delivery.
This pull removes the requirement for scheduling at
each stage, and hence the buffer stocks and Work
In Progress that populate the ‘Push’ Process Chain.
Notes: <number>
(READ SLIDE)

## Slide 19: Takt, an Enabler for Work Balance
Notes: <number>
You are the owner of a café.
In order that you deliver consistent quality of product to your customers, and ensure that you staff work in a safe manner you have introduced Standardised Work for your product, a cup of coffee.
The work is mapped on a Standardised work process sheet.
There are 7 steps to production. Times are divided into working and walking.
Each OP has an OP sheet that describes in full detail the exact manner that it should be carried out, identifying all parts, tooling, process steps etc. These Op sheets are identified by the Op numbers.
(Click through the sheet explaining each step and how it is recorded on the process sheet)

## Slide 20
440 minutes/day X 60 seconds/minute
380 products per day
=
66 Secs
The Customer Requires: 380 Mugs of Coffee / day
Time Available
Customer Demand
=
TAKT TIME
Takt, an Enabler for Work Balance
Time Available = 480mins - 30mins breaks - 10mins team meeting
Notes: <number>

## Slide 21
66 Secs TAKT
Non Value Added
Value Added
C01
C02
C06
C03
(Add Coffee)
C04
Add Milk
C05
(Add Water)
Takt, an Enabler for Work Balance
Op
No
7 Secs
2 Secs
8 Secs
2 Secs
8 Secs
4 Secs
14 Secs
12 Secs
Notes: <number>

## Slide 22
Takt, an Enabler for Work Balance
How do we use this information to meet our
customer demand?
Add 20% more workers?
Run 20% Overtime?
Contract out 76 cups of coffee to a supplier?
Use Takt to drive waste elimination
Customer Demand +20%
380 mugs / day to 456 mugs / day
Notes: <number>

## Slide 23
380 Mugs of Coffee
440 X 60
380
=
66 Secs
TAKT
When Customer requirements change, Takt changes
Takt, an Enabler for Work Balance
456 Mugs of Coffee
440 X 60
456
=
55 Secs
TAKT
Notes: <number>

## Slide 24
66 Secs
Non Value Added
Value Added
C01
C02
C03
C04
C05
Takt for 380 mugs / day
C06
55 Secs
Takt for 456 mugs / day
Takt, an Enabler for Work Balance
Notes: <number>

## Slide 25: Takt, an Enabler for Work Balance
Notes: <number>

## Slide 26: Takt Time
Customer
REMEMBER WASTE, ITS DOOM
We know why conventional western methods will
make our business unprofitable
Notes: <number>
READ SLIDE - REFRESHER

## Slide 27: Takt Time
WASTE
Enables work-balancing
Enables Flow
Driving out waste within our business
TAKT TIME
Notes: <number>
READ SLIDE - SUMMARY

## Slide 28
www.BeyondLean.com
Thank You!