## Slide 1: Lean Six Sigma Certification & Training
Module 014 Section 004
TPM Overview

## Slide 2: Beyond Lean Online Resources
        Certification Courses and Exams
        Workbook Downloads
        Membership Online Training Videos
        LeanSigma Fast Action Implementation Guide
Order Support Products Here

## Slide 3
Improvement Activities
Planned Maintenance
Autonomous Maintenance
Education & Training
Maintenance Prevention
Continuous Improvement
Systematic Elimination of Waste
TPM
What is Total Productive Maintenance (TPM)?
© www.beyondlean.com
Notes: <number>
The widely accepted pillars of TPM -
  - Improvement Activities
  (embedded in all TPM key drivers in APS)
  - Planned Maintenance
  (covered in Effective Maintenance in APS)
  - Autonomous Maintenance
  - Education & Training
  (embedded in all TPM key drivers in APS)
  - Maintenance Prevention
  (covered in Effective Maintenance in APS)
All supported on a firm foundation of Continuous Improvement and the Systematic Elimination of Waste.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 4: What is Total Productive Maintenance (TPM)?
A system of maintenance covering the entire life of the equipment and the total human resource.
TPM is a tried and tested way of eliminating waste, saving money and making factories better places to work.
It gives operators the knowledge and confidence to manage their own machines.
TPM is a long term process to increase skills, raise efficiency and achieve zero losses.
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
© www.beyondlean.com
Notes: <number>
TPM can be the foundation for improvement for an entire production process.
It is not just another maintenance program, it requires co-operation at all levels and function within the business. Team activity is crucial in both the development and continued success of TPM.
It means breaking down traditional attitudes to specialist roles and the establishing of an “up-skilling” program for operators and maintainers.
TPM means –
- Building and improving equipment so that it won’t breakdown, produce defects or have minor stoppages.
- Training operators to be capable of detecting equipment defects, implementing inspection and lubrication for maintenance.
- A work place where equipment is easy to use, work can be done both easily and safely, and with a high productivity.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 5: What are the benefits of TPM?
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
TPM refuses to accept that machine inevitably fail.
TPM reduces the total life-cycle costs of equipment.
TPM simply reminds us that every time a machine fails, something could have been done to prevent it.
Gradually the operator’s become maintainers.
Gradually the maintainers become improvers.
TPM develops the five senses, as well as technical skills.
© www.beyondlean.com
Notes: <number>
Zero Breakdowns – Zero Accidents – Zero Defects.
Philosophies that could and should be considered across all aspects of the business, that: “failure is not inevitable and something could have been done to prevent it”.
  WHAT WILL STOP IT HAPPENING AGAIN?
TPM helps break down barriers to best practice by removing specialisation.
Maintainers benefit from “up-skilling” of operators as they are able to focus attention on improving preventative measures and removing waste from the life-cycle of equipment.
Breakdowns may be sudden but the signs are often there well before the machine finally ceases to run, i.e. unusual sounds, vibrations, etc.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 6: Loss Elimination through TPM?
Available time
Available operating time
Actual operating
time
Effective operating time
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Equipment
Six Big Losses
© www.beyondlean.com
Notes: <number>
Animation - Activate randomly as you talk through.
TPM will focus on the 6 big losses that impact Availability, Productivity and Quality.
Breakdowns and Set Ups reduce the “Available Time” that operators have to add value during “Operating Time”.
Further stoppages and factors which effect the most effective use of that “Operating Time”, are Idling, Minor Stoppages and Speed Losses, i.e. tool breakages, swarf clearance (<10 mins) and the effect of equipment not running to optimum speeds.
This “Actual Operating Time” is then finally lessened by the impact of Defects (Rework) and Start Up Losses (both in quality and delays achieving optimum conditions).
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 7: What is Effective Maintenance?
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
PLANNED MAINTENANCE
“ The scheduling of maintenance activities on a time based or usage basis regardless of the current performance levels of the equipment”
PREVENTATIVE MAINTENANCE
“ A systematic approach to eliminate catastrophic failure/breakdowns through regular care and attention, early diagnosis and rectification”
PREDICTIVE MAINTENANCE
“ A systematic approach utilising history and equipment condition monitoring to predict and prevent catastrophic failure/breakdowns ”
© www.beyondlean.com
Notes: <number>
It is not :- “Repairing equipment as quickly and efficiently as possible when it breakdowns“
It is :- “Minimising the chances of equipment ever breaking down, ensure it runs as effectively as possible and repairing it as quickly and efficiently as possible if it does “
All the activities within Effective Maintenance systems require close working partnerships with operations. We must not accept the arguments that:-
  “Its running all right at the moment, lets leave it”
  “We can’t spare the time for planned maintenance”, etc.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 8: What is Effective Maintenance?
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
BREAKDOWN MAINTENANCE
“ When all else fails ensuring that equipment availability is achieved in the shortest possible time whilst eliminating root cause faults with sustainable repairs”
EFFECTIVE EQUIPMENT DESIGN
“ A systematic approach to equipment design which maximises equipment availability, minimises life cycle costs and eliminates waste”
© www.beyondlean.com
Notes: <number>
Machines will inevitably still breakdown as a TPM system strives towards maturity, when they do fail we must not revert to the “Quick Fix”.
By all means instigate immediate customer protection, but root cause investigation and elimination must be the goal.
Assess current production requirements and consider value added planned maintenance in parallel with breakdown repairs.
Why wait until equipment is in service before we consider how to maximise its availability. Ensure equipment is designed with maintainability and reliability as the watch words.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 9: What is Autonomous Maintenance?
An operator skills development programme.
Allows problems to be identified and solved quickly.
Stops accelerated deterioration of plant and equipment.
An approach to stop deterioration related failures.
Stabilises equipment conditions (standards).
Develop training materials on how to run, operate & maintain equipment.
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
© www.beyondlean.com
Notes: <number>
The primary way in which production departments play a part in TPM is through Autonomous Maintenance.
Operators systematically trained in a step-by-step process for cleaning, checking and making minor adjustments on the equipment they work with.
Bring operators and maintainers together for a common goal.
Early detection and treatment of abnormal conditions.
Up skill program for operators.
      NOT:- “I run, you fix”
Assess current production requirements and consider value added planned maintenance in parallel with breakdown repairs.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 10: What is Overall Equipment Effectiveness (OEE)?
Overall Equipment Effectiveness (OEE) is a total measure of performance that relates the availability of the process to the productivity and quality.
OEE is the Key Performance Indicator (KPI) for TPM.
OEE will measure the impact of change on a process caused by eliminating process, or equipment losses.
A World Class Company should achieve 85% OEE on key equipment
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
© www.beyondlean.com
Notes: <number>
If you were told that equipment effectiveness in your department was 95% you might reasonably assume that the equipment was running efficiently and effectively
How is that measured ? What does it take account of ?
What if the equipment was 95% effective and this meant it ran for 95% of the time? Still impressed ? Is it still a good measure ?
What if it ran for 95% of the time but had 50% scrap ?
TPM is a shift from traditional accounting measures of performance.
Still impressed? I thought not!
OEE is the KPI for TPM that combines availability, productivity and quality to give a total measure of a machines performance.
Provides the focus for eliminating waste through reducing losses.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 11: What is Quick Changeover?
Quick Changeover is a method of analysing and reducing the time needed to change a process from producing one good part to producing the next good part part.
It is a driver for standardisation.
It is one of the 6 Big Losses.
Quick changeovers are an enabler for flow.
Often referred to as “Single Minute Exchange of Die” (SMED).
Maintenance of normal conditions / Early discovery of abnormalities / Prompt response
© www.beyondlean.com
Notes: <number>
REDUCE - COMBINE - ELIMINATE
Often too much emphasis is placed on reducing machining times when the impact of long changeovers is much more of an impact.
Changeovers outside TAKT, hinder flow.
Adjustments tend to take up the majority of the time during a changeover – Necessary and Unnecessary.
Divide work content into “Internal” and “External” activities –
  Internal : Those activities that can only be done whilst the machine is not producing.
  External: Those activities that can be done whilst the machine is cycling.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 12: What will TPM do for your business?
IMPROVE PLANT AND EQUIPMENT
IMPROVE CORPORATE CULTURE
IMPROVE HUMAN RESOURCES
© www.beyondlean.com
Notes: <number>
Through educating and developing the workforce in Lean Manufacturing -
We can improve plant and equipment -
The culmination of both these factors will lead to an improvement corporate culture.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 13
www.BeyondLean.com
Thank You!