## Slide 1: Lean Six Sigma Certification & Training
Module 01 Section 005
Control Overview

## Slide 2: Beyond Lean Online Resources
        Certification Courses and Exams
        Workbook Downloads
        Membership Online Training Videos
        LeanSigma Fast Action Implementation Guide
Order Support Products Here

## Slide 3: Control Overview
During the Improve phase, the solution was piloted, and plans were made for full-scale implementation
Putting a solution in place can fix a problem for a period, but in order to ensure that lasting improvements are maintained it is important to put controls in place to monitor performance and take corrective action where necessary
The steps of this phase are equivalent to the steps one would take in setting up a Process Management System. If your process already exists in the PMS then it should just be a question of updating the relevant PMS documents for the process in question
The control plan should have been defined in the Improve phase, this phase (in part) is about the implementation of the control plan
Notes: <number>

## Slide 4: Control Checklist
To complete the control phase ensure:
  Complied results data confirming that our improvement as achieved the Goal defined in our DMAIC charter
  Selected on-going measures to monitor performance of the process and continued effectiveness of our solution
  Determined key charts/graphics for a ‘process scorecard’ on this process
  Prepared all essential documentation of the revised process, including key procedures and process maps
  Identified an ‘owner’ of the process who will take over responsibility for our solution and for managing continuing
  Developed (with the Process Owner) Process Control System (PCS) detailing requirements, measures, and responses to problems in the process
  Prepared a story board documenting the team’s work and data collected during the project
  Forwarded other issues / opportunities which we were not able to address to Senior Management
  Communicated project success to the external environment
Notes: <number>

## Slide 5: Control Steps
Step 13:
Implement and Standardise the Solution
Step 14:
Implement Process Control System
Step 15:
Assess Achievements and Lessons
Toll Gate Review
Notes: <number>

## Slide 6: Step 13: Implement and Standardise the Solution
Standardisation is what allows high quality to happen on a reliable, sustained basis
Standardisation is making sure that important elements of a process are performed consistently in the best possible way. Changes are only made when data show that a new alternative is better
Uses for standard practices:
  Reduce variation among individuals / groups (Y becomes more predictable)
  Provide “Know-why” for operators and managers on the job
  Provide a basis for training new people
  Provide a trail for racing problems
  Provide a means to capture and retain knowledge
  Give direction in the case of unusual conditions
Notes: <number>

## Slide 7: Step 13: Implement and Standardise the Solution
In completing step 13, you should produce at least the following:
  The full implemented solution
  A system to ensure the new process is standardised as appropriate
  Set of procedure documents, associated forms, check-sheets, visual aides, support tools etc.
Notes: <number>

## Slide 8: Step 13: Implement and Standardise the Solution
A few tools are applicable to this step:
  5 S
  Procedure Documents etc.
Notes: <number>

## Slide 9: Step 13: Plan the Work, Work the Plan
During step 12 you should have planned the implementation of the solution.
Implementing the solution should therefore be straightforward. As the implementation rolls out ensure you have the appropriate:
  Communications and regular or exception reporting process
  Issues and risk management mechanism
  Level of scheduling and project stage management
  Budget control
  Configuration management of deliverables
Notes: <number>

## Slide 10: Step 13: Implement the Solution: Training
Unless change is integrated into the day-to-day operations of the enterprise, change is unlikely to survive for long
Prior, during and after, you need to make sure that everyone using the new process is trained in the new methods and/or systems
Even experienced employees need to be trained in the new methods
Notes: <number>

## Slide 11: Step 13: Implement the Solution: Training
Do not try to develop a single training session to teach people everything they may ever need to know about the job:
  Focus on the most critical aspects
  Explain the reasons for the changes
  Combine up front training with support
  Not everybody learns at the same pace
  Most learning will occur on the job (especially Six Sigma!)
Notes: <number>

## Slide 12: Step 13: Standardise the Solution with 5S
5S is the Japanese concept for house keeping:
  Seiri – sort
  Seiton – straighten / Set in Order
  Seiso – shine
  Seiketsu – standardise
  Shitsuke – sustain
5s has been adopted as ‘lean’ method to bring about:
  Process standardisation,
  Improvement and efficiency
Notes: <number>

## Slide 13: Step 13: Translation of the 5 steps of 5S and definitions
English
Japanese
Waste identification and elimination
Increase flexibility and foundation for continuous improvement
SORT
STRAIGHTEN
SHINE
STANDARDIZE
SUSTAIN
SEIRI
SEITON
SEISO
SEIKETSU
SHITSUKE
Variability reduction and control
  Eliminate all non-essential tools, materials from the workplace
  Regularly clean the workplace and equipment
  Develop standard procedures and checklists to maintain an orderly, clean, and functional work area
  Organize all necessary tools, materials
  Assign an optimal area in the workplace
  Implement systems to monitor and maintain to ensure the workplace is improved and 5S becomes part of the culture
Notes: <number>

## Slide 14: Step 13: Step 1 - Sort
  Determine what is necessary in the workplace, remove other items
  Determine storage location based on frequency of use
  Use only 1 organisation method within the company to create immediate visibility and response (i.e., tagging method)
    -Utilize red tags to properly identify item for removal
    -If there is a question, use a yellow tag which requires further review
  When in doubt, throw it out
  Organize only what is needed, in the amount needed, when it is needed
Maintenance of improved condition
Waste identification and elimination
Sort
Straighten
Shine
Standardize
Sustain

## Slide 15: Step 13: Step 1 - Sort
Remove anything which isn’t needed for current work
Key: Leave only the bare essentials
Ask Yourself:
  What do we need?
  What don’t we need?
  What can we remove?
  What can we throw away?
  What can I reorganise?
Notes: <number>

## Slide 16: Step 13: Step 1 - Sort
Used daily
Supports production
Correct quantity
Frequency
Urgency
Quantity
Store
off-line
Remove
or tag
Keep
Never used
Not required for production
Excess quantity
Item used ?
Yes
Some times
No
Sometimes used
Supports production
Excess quantity
Potential unnecessary items
  Stock (raw material, WIP, finished products)
  Facilities (equipment, tools, carts, pallets, work tables, etc.)
  Locations (floor, kitchens, rooms, etc.)
  Machines (production equipment, office equipment)
  Documents (reports, charts, etc.)
  Stationery (paper, pens, clips, etc.)
Notes: <number>

## Slide 17: Step 13: Step 2 - Straighten
Maintenance of improved condition
Waste identification and elimination
Sort
Straighten
Shine
Standardize
Sustain
  Plan an optimum layout
  Reconfigure the area to match the planned layout
  Use floor tape to mark the new locations for all equipment, racks, production materials, etc., as well as aisles
  Determine the best location for tools, gauges, work aids, and other small items
  Mark and label all locations
  Build or install racks for frequently used items
  Store items close to their points of use
  A place for everything and everything in its place
  Visual controls communicate information about the work area
  Eliminates Searching

## Slide 18: Step 13: Step 2 - Straighten
A Place for Everything and Everything in its Place
Arrange items so they are
  Easy to find
  Easy to use
  Easy to put away
What do I need … Where should it be?
Notes: <number>

## Slide 19: Step 13: Step 3 - Sanitize
Maintenance of improved condition
Waste identification and elimination
Sort
Straighten
Shine
Standardize
Sustain
  Clean the entire work area including floors, walls, equipment, etc.
  Tag any leaks, broken dust guards, etc. Make sure that anything that has been tagged is repaired as soon as possible
  Restore the equipment to its original functional condition
  Paint or refinish areas
  Assure that the proper cleaning tools are present to maintain the improved condition
  Assure that proper collection methods exist for normal work debris and trash
  Maintaining everything in top condition enables it to be used at any time
  Clean work environments relieve frustration and stress
  Daily cleaning should be a part of the normal work routine
  Relieves stress and strain – when something needs to be used, it is in good working order
  Increases work efficiencies

## Slide 20: Step 13: Step 3 - Shine
Housekeeping
Inspection
5 minute shine
Everything is ready to use
A clean workplace enhances quality, safety and pride
Notes: <number>

## Slide 21: Step 13: Step 4 - Standardize
Maintenance of improved condition
Waste identification and elimination
Sort
Straighten
Shine
Standardize
Sustain
  Establish a standardized approach
  Define what needs to be done on a regular basis to maintain the work area
  Determine the intended frequency – classify as daily, weekly, monthly, and semiannually (other time increments may be used)
  Use this information to write standardized 5S checklists
  Decide who should be responsible
  Incorporate the content of the checklists into standard work instructions
  Ensure that the first 3 steps are maintained
  Create and develop organisation
  Develop 5S discipline
  Provide a baseline for improvement

## Slide 22: Step 13: Step 4 - Standardize
Build on What You’ve Done
Establish a standardized approach
  Decide what should be cleaned, sorted and straightened (targets)
  Decide the standard parameters and settings that are to be maintained
  Decide who is responsible for each task
  Decide what tools are appropriate for each task
  Decide what methods will be used (i.e., Visual Management: signs for instructions, information etc.)
This step goes hand in hand with developing procedures and forms
Notes: <number>

## Slide 23: Step 13: Step 5 - Sustain
Maintenance of improved condition
Waste identification and elimination
Sort
Straighten
Shine
Standardize
Sustain
  Develop a 5S audit sheet as a guideline
  Establish an audit schedule
  Perform regular 5S audits
  Divide the plant into different areas and assign 5S responsibility
  Involve operators, supervisors and managers in 5S audits on a regular basis (possibly monthly)
  Post audit results
  Implement the audit process
  Involve all associates
  Develop 5S habits
  Begin integration with other functions for maintenance and quality

## Slide 24: Step 13: Step 5 - Sustain
Self discipline and motivation are vital to 5S success
Sustain:
  Awareness & focus
  Rewards & recognition
  Satisfaction & enthusiasm
Conduct self audit to ensure adherence to earlier 4Ss
Notes: <number>

## Slide 25: Step 13: 5S Q&A
Typical Question | Response
Why should a company dedicate time and resources to an individual improvement program whose principles are as simple as having a useful, orderly, clean work area? Are these not common sense principles that can be easily applied without the use of a standard 5S program? | Although 5S principles are very simple, history and experience have clearly shown that they are almost impossible to maintain without the use of a standardized system. Years of misperceptions about the significance of 5S has led to years of processes working at lower-than-optimal efficiency levels
How does the implementation of a 5S program allow an office to become more productive and efficient? | A properly maintained, optimised workplace can provide employees with an environment containing minimum variability and disruption, leading to increases in productivity and efficiency
Why is the 5S program frequently cited as a key element of an overall continuous improvement system? | Most systems for continuous improvement involve finding the best procedure and standardizing it. By minimizing variability and disruptions, 5S allows these standardized procedures to be followed appropriately
How quickly can cost reductions be shown from the implementation of a 5S program? | Although a 5S program will save money for most companies, the savings are indirect and can mainly be recognized as long-term cost savings tied to associated shop floor improvement programs
What will it take in terms of financial resources and capital spending to implement a 5S program? | A minimum amount of spending is required to implement a 5S program. This usually includes the cost of paint, labels, etc., as well as the cost of moving equipment and the cost of repairing small equipment problems. Labour will also be required to make and maintain improvements
Common sense isn’t all that common!
Notes: <number>

## Slide 26: Step 13: Procedures and Other Relevant Documentation
Procedures, forms etc. need to be written down, audited and kept up to date
Consider the following when designing procedures and forms :
  Keep them simple and that they contain only the pertinent information to do the job
  Graphics, flowcharts etc. can sometime express more information than words alone
  Examples generally work well
  Must be user friendly, get them reviewed by the user first
Notes: <number>

## Slide 27: Step 13: Ownership Documentation
Procedures, forms etc. are the responsibility of the Process Manager (see later), NOT the Project Manager or Analyst
An Analyst can help put the documentation together initially, but they must ultimately be owned and maintained by the business
The process model sits above the procedures and is used to manage and analyse the end to end process; procedures cover specific work instructions within the process, and should include a reference to the parent process for consistency
Process / procedure ownership has got to be the most thankless job going (unfortunately), due to common management misconceptions … look out for Teflon shoulders!!!
Notes: <number>

## Slide 28: Control Steps
Step 13:
Implement and Standardise the Solution
Step 14:
Implement Process Control System
Step 15:
Assess Achievements and Lessons
Toll Gate Review
Notes: <number>

## Slide 29: Step 14: Implement Process Control System
A process control system helps to maintain the gain that occurs when / after implementing a solution
The process control system consists of four key responsibilities:
  Defining the process & performance measures
  Measuring the process
  Controlling the process by providing a response plan
  Continually improving the process over time as a day-to-day management responsibility
Notes: <number>

## Slide 30: Step 14: Implement Process Control System
In completing step 14, you should produce at least the following:
  A documented system that ensures the on-going monitoring, control, and management of the new
  The necessary control documents such as:
    Process Catalogue
    Process Models
    Process Control System (PCS)
    Measurement Plan
    Statistical Process Control (SPC)
    FMEA
    ABC Models
    Performance Charts/Dashboards
Notes: <number>

## Slide 31: Step 14: Implement Process Control System
A few tools are applicable to this step:
  Process Models
  Process Control System (PCS)
  Measurement Plan
  Statistical Process Control (SPC)*
  FMEA*
  ABC Models*
  Performance Charts/Dashboards
Notes: <number>

## Slide 32: Step 14: Process Management Roles & Responsibilities
PROCESS
SPONSOR
PROCESS
OWNER
PROCESS
MANAGER
member of the senior management team
advocate and ambassador for the overall process
member of the operational management team
owns the overall sub-process
advocate and ambassador for the overall sub-process
member of line management staff
specific line and functional responsibility & accountability
impacts on overall sub-sub-process
champions the process internally and externally
provides strategic direction for the process
process design, operation and performance
ensures process design reflects needs
sets targets
ensures adequate resourcing
ensures continuous process improvement
benchmarks with other organisations
manages and resolves interface and integration issues
continually monitors the process
accountable for the performance of the process in achieving targets
provides appropriate performance data
responsible for procedures etc. being up-to-date
Notes: <number>

## Slide 33: Step 14: Key Steps of Process Management
Improve Process
Measure Process
Define Process and Measures
Control Process
Execute
Process
Process Performance
Process Improvements
Process & Measure Definitions
Performance Data
Response Plans
Customer Requirements & Business Needs
‘Execute Process’ is shown as a different shape because execution is not a process management responsibility
Notes: <number>

## Slide 34: Step 14: Define Process and Measures
Defining a process creates the disciplined environment required for controlling and improving the process
Management’s responsibility to define each process inherently includes the responsibilities for implementing and sustaining the process
Most of this work should have been done during the define and improve stages of the DMAIC project
Define Process & Measures
If it is not written down, it does not exist!!
Notes: <number>

## Slide 35: Step 14: Define Process and Measures
The key objectives associated with defining, implementing, and sustaining are:
  Design processes that meet or support business and customer objectives (CTQcs and CTQbs)
  Identify the critical issues / control points that relate to the performance of the process (process measures)
  Provide the infrastructure/mechanisms (methods, people) that support the process
  Ensure the organisation has the ability to execute and sustain the processes (skills, training, tools, facilities etc.)
When selecting measures, you will probably want to retain the original project Y, but the new process may require different xs that will require monitoring for control purposes
Notes: <number>

## Slide 36: Step 14: Define Process and Measures
Mandatory tools for this aspect of process management include:
  Process model
  Measurement Plan / Process Control System
  List of associated procedures, work instructions etc.
Other useful tools include:
  Paper based description of the process model to record systems, staff, policies, procedures etc.
  ABC model for costing purposes
  FMEA to capture critical failure modes and controls
Notes: <number>

## Slide 37: Step 14: Measure Process
Measures are the basis for detecting deviations from acceptable performance. They are also the basis for identifying opportunities for process improvement.
The key objectives of process measurement are to:
  Collect data that measure the performance of the process
  Analyse the performance of each measure
  Retain and use the data to:
    Assess process stability and capability
    Interpret the results of observations and analyses
    Predict future costs and performance
    Provide baselines and benchmarks
    Plot trends
    Identify opportunities for improvement
Measure Process
Notes: <number>

## Slide 38: Step 14: Measure Process
The main output from measuring the process are performance charts / dashboards
The Measurement Plan should define the measures, how they are to be collected, stored, and analysed
As with process standardisation, it is vital that the collection, display and analysis of the data is also standardised as much as possible
It is the responsibility of the process manager that process measures are sustained, collected consistently, and the process improved where possible
Notes: <number>

## Slide 39: Step 14: Control Process
Controlling a process means keeping the process within (inherent) performance boundaries – that is, making the process behave consistently. This involves:
  Measurement: obtaining information about processes
  Detection: analysing the information to identify variations in the process that are due to assignable cause
  Correction: taking steps to remove variation due to assignable cause
Control Process
Notes: <number>

## Slide 40: Step 14: Control Process
The spectrum of tools for process control can be quite large and can incorporate one or more of the following examples:
  Qualitative Control
    Process Reviews: formal or informal reviews with actions recorded and tracked through a log of some description (or not!)
    FMEA: in addition or instead of process reviews, the on-going management of process failure modes
  Quantitative Control
    SPC: The ultimate in process control, but does take a degree of sophistication to make it work effectively
    Process Capability Analysis: Often done in conjunction with SPC
    Process Control System (PCS): Quality Control Charts are an extension of the measurement plan, they indicate where in the process a check needs to be made, and the necessary corrective action if a measure is outside of its specification
Select the tools most appropriate to the process, and to the capabilities of the organisation itself
Notes: <number>

## Slide 41: Step 14: PCS (QC Charts)
A PCS chart is a little more than an extension of Deming's Plan-Do-Check-Act cycle:
Plan / Do:
Typically a flowchart
Check:
Describes what you will check in the process to monitor its quality
Act:
Response Plan, how will operators / managers react depending on what they find in the measures
1
2
3
Notes: <number>

## Slide 42: Step 14: SPC & Capability Analysis
We explored SPC during the Analyse phase as a way to examine process stability and capability to assess how well the process was meeting customer requirements
As mentioned previously, SPC is best suited for on-going process management:
  Create control charts for key process measures
  If the process is out of control, or not capable improve the process
  When the process is in control and stable, monitor for out of control conditions and take action only when necessary
  New improvements should improve the average and / or reduce control limits (variation)
Notes: <number>

## Slide 43: Step 14: SPC & Capability Analysis Summary
To interpret data you need a method of analysis
Variation undermines simple comparisons such as this week v. last week
Notes: <number>

## Slide 44: Step 14: SPC & Capability Analysis Summary
In many organisations, specifications are usually arbitrary numerical targets rather than genuine customer requirements
The specification approach does not consider the ‘voice of the process’
Managers attempt to attach a meaning to each and every value or data point
Notes: <number>

## Slide 45: Step 14: SPC & Capability Analysis Summary
There are 3 ways to meet a goal:
  Improve the process
  Distort the process
  Distort the data
Notes: <number>

## Slide 46: Step 14: SPC & Capability Analysis Summary
The control chart concentrates on the behaviour of the underlying process
It defines the ‘voice of the process’
It enables management by fact
Notes: <number>

## Slide 47: Step 14: Juran’s Trilogy, SPC, and PCS!!!
X
New Zone of Quality Control
X
Sporadic Spike
Chronic Waste
Quality Improvement
Original Zone of Quality Control
Time
Define Process and Measures
(Quality Planning)
Control Process
(Quality Control)
Improve Process
(Quality Improvement)
Measure Process
(Quality Control)
Notes: <number>

## Slide 48: Step 14: Improve Process
Even though a process may be defined and under control it may not be capable of meeting customer needs or business objectives. In either case, the key objectives of improving a process are to:
  Understand the characteristics of the existing process and the factors that affect process capability
  Plan, justify, and implement actions that will modify the process to better conform to customer and business requirements
  Assess the impacts and benefits gained, and compare these to the costs of the changes made to the process
Improve Process
Notes: <number>

## Slide 49: Step 14: Improve Process
Improving a process is required when your control system / review etc. indicates that the process if failing to meet or is forecast to fail to meet the customer and/or business requirements
Upon detection, improving the process can be facilitated in a variety of different ways:
  As business as usual: An action is raised in the appropriate process log or in the Process Catalogue (if you are using one) and tracked through to completion
    Best suited to small changes, or ones requiring little or no expenditure
    Ensure all process documentation is kept up to date
  As a ‘change’ project: For large scale changes consider:
    Another DMAIC project, but only if it meets the Six Sigma criteria (see earlier presentation)
    Or another suitable method
    In either case ensure all process documentation is kept up to date
Notes: <number>

## Slide 50: Step 14: Document the PMS / Control System
If you have a corporate or divisional Quality Management System (QMS) (e.g. ISO, PE), it should detail how process control should be applied to your to your processes
If you do not have a QMS then a process catalogue with a statement of how the control system should operate should suffice
If you do not have a process catalogue (or in addition) you should produce a process control plan that dictates how the process is to be defined, measured, controlled and improved
Regardless of the mechanism used you need to specify the what's, why’s, when’s, how’s, and who’s
Notes: <number>

## Slide 51: Control Steps
Step 13:
Implement and Standardise the Solution
Step 14:
Implement Process Control System
Step 15:
Assess Achievements and Lessons
Toll Gate Review
Notes: <number>

## Slide 52: Step 15: Assess Achievements and Lessons
The solution has been implemented, and some form of control system has also been established
The PCS will monitor on-going process performance and make continuous process improvement a part of the day-to-day operations
From a project point of view we need to take stock of what has changed, assess if the solution has lived up to expectations, and formally shut the project down
Notes: <number>

## Slide 53: Step 15: Process Management vs. Project Management
Be aware that this step is crossing over from the project management environment into operational management environment:
Improve Process
Measure Process
Define Process and Measures
Control Process
Execute
Process
Execute
Plan
Process
Measure Plan/Actuals
Define Plan
Adjust plan
Requirements
Service
/ Products
Process Management
Project Management
Notes: <number>

## Slide 54: Step 15: Bringing Home the Bacon…
Realising project benefits…
Define
Budget:
Initial COPQ estimates
Outline business case
Forecast:
Update COPQ based on To-Be Process
Add actual solution costs to the business case
Actual:
Actual cost savings
Measure
Analyse
Improve
Control
Forecast:
Update COPQ estimates based on analysis of real data
Forecast:
Update COPQ estimates based on real data
All our hard work should be paying off through actualized savings!! Make sure these saving are captured to justify the project expense and to compare against original estimates and budget
Notes: <number>

## Slide 55: Step 15: Assess Achievements and Lessons
In completing step 15, you should produce at least the following:
  Evidence the project has worked, or an estimate of when that assessment can be made
  Recommendations about further opportunities
  Project closure document
  Lessons learnt report
Notes: <number>

## Slide 56: Step 15: Assess Achievements and Lessons
A few tools are applicable to this step:
  Story board
  Final report
  Project closure document
  Lessons learnt report
  Follow on action recommendations
Notes: <number>

## Slide 57: Step 15: Assess Achievements and Lessons
Ensure the project has delivered
Establish a clear mechanism for the on-going management of process performance
Apply the learning and opportunities for further improvement
Notes: <number>

## Slide 58: Step 15: Assess Achievements and Lessons
Key questions:
  How well do the results match the expectations?
  What’s the data telling you?
  How well did the plan work?
  How can the solution be improved?
  Is there scope for prevention?
Notes: <number>

## Slide 59: Step 15: Story Board
A tool that communicates the project clearly an concisely to the board and other interested parties:
  Not ‘War and Peace’ – a couple of slides per phase
  Update as you go along and it won’t be a hassle to prepare
  For example – an ‘A3 Report’
Notes: <number>

## Slide 60: Step 15: Final Report
The final report is a detailed report of each project phase:
  Provide a clear rationale for the project, the main problem statement, and the original objectives
  Detail the approach taken and the main findings discovered during the define / measure phases
  The analysis section should be summary but reference the original data sources or provide an appendix for future analysis / comparisons
  Provide a clear rationale for the selection of the solution
  Provide a definitive statement about the benefits achieved from the implemented solution and a comparison against the original objectives / performance statement
For expediency you could roll ‘lessons learnt’, ‘project closure’ etc. documents into the one report
Notes: <number>

## Slide 61: Step 15: Lessons Learnt Report
Pass on any lessons that can be usefully applied to other projects:
  What management and quality processes:
    went well
    went badly
    were lacking.
  A description of any abnormal events causing deviations
  An assessment of technical methods and tools used
  An analysis of project Issues and their results.
  Recommendations for future enhancement or modification of the project management method.
  Useful measurements on how much effort required during the project
Notes: <number>

## Slide 62: Step 15: Follow on Action Recommendations
To pass details of unfinished work or potential product modifications to the group charged with future support of the final process in the operational environment:
  Requests for change that were considered to have merit but were not implemented during the project
  Off-Specifications recording missing products or products that do not meet the original requirements
  Risks identified during the project, which may affect the process in its operational life
  Any identified hand-over or training needs
  Any other activities needed to improve the process
  Considerations for other related projects
Notes: <number>

## Slide 63: Control Summary
Step 13:
Implement and Standardise the Solution
Step 14:
Implement Process Control System
Step 15:
Assess Achievements and Lessons
Toll Gate Review
Notes: <number>

## Slide 64
www.BeyondLean.com
Thank You!