## Slide 1: Lean Six Sigma Certification & Training
Module 03 Section 005
OEE – Overall Equipment Effectiveness

## Slide 2: Beyond Lean Online Resources
        Certification Courses and Exams
        Workbook Downloads
        Membership Online Training Videos
        LeanSigma Fast Action Implementation Guide
Order Support Products Here

## Slide 3
Introduction
Overall Equipment Effectiveness Overview
Measuring OEE / 6 Big Losses
Data Collection
How to Eliminate Losses
What are the benefits?
Contents
Notes: <number>
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 4: What is OEE ?
Overall Equipment Effectiveness (OEE) is a total measure of performance that relates the availability of the process to the productivity and quality
Notes: <number>
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 5: What does that mean ?
OEE is a Key Performance Indicator (KPI) that can measure the impact of change on a process caused by eliminating process, or equipment losses
Notes: <number>
OEE is used to measure the performance of equipment and the process not the operator.
It can be used to take a snap shot of equipment performance and enables trends, peaks and troughs to be plotted.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 6: Why is OEE so important ?
If you were told that your department was running flat out you might reasonably assume that the equipment was running efficiently and effectively.
What if the equipment only ran for 75% of the time?
What if when it ran it ran at 80% of its speed ?
What if only 90% of the parts it made are good?
Individually these performance measures seem to indicate an OK piece of equipment, but is it a true picture?
What’s impacting on these performance figures?
Notes: <number>
1st Animation - If you were told…….
2nd Animation - What if the equipment…..
3rd Animation - What if when it ran……..
4th Animation - What if only …….
5th Animation - Individually these …….
6th Animation - What’s impacting ……..
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 7: How do I measure OEE?
OEE =
AVAILABILITY
x PRODUCTIVITY
x QUALITY
Notes: <number>
OEE is simply a combination of three other measures - availability, productivity and quality, which by themselves do not tell the full story.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 8: OEE and the Six Big Losses
Equipment
Six Big Losses
Available time
Available operating time
Actual operating
time
Effective operating time
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Total Available time
Planned Downtime
Notes: <number>
Animation - Activate randomly as you talk through.
An ideal manufacturing environment means that equipment will be available to use when you want to use it!
Typically the “Effective Operating Time” is limited by a number of key reasons.
From the “Total Available Time” first take the “Planned Downtime”, such as breaks, planned maintenance, no scheduled work, etc.
Waste restricts the “Available Time” even further
Collectively these key waste elements which effect Availability, Productivity and Quality, are known as the “6 Big Losses”.
These losses effect the “Available Time” in the following manner.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 9: Availability
“The percentage of time equipment is actually running when we need it”
AVAILABILITY= AVAILABLE TIME – UNPLANNED DOWNTIME x 100%
        AVAILABLE TIME
Where:-
Available Time = Total Available Time – Planned Downtime*
Available time
Available operating time
Breakdowns
1
Setup / adjustment
2
*Note :- Planned Downtime could be PM, no scheduled work, breaks, etc.
Notes: <number>
Introduce the equation in basic terms.
1st Animation - Available time
Starting with the Total Available time (this could be for a fixed time period (3 hrs), the full shift, 24 hours, etc.), less the time that you don’t wish to be considered, such as planned breaks, meetings and maintenance.
To give you the Available time.
2nd Animation - Available operating time
The Available operating time is, therefore, the Available time less
Breakdowns and Setup / Adjustment.
Prior to next slide ask for examples of Planned v Unplanned Downtime.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 10: Planned v Unplanned Downtime
Planned
  Excess capacity.
  Planned breaks.
  Planned Maintenance.
  Communications briefs / team meetings.
Unplanned (Losses)
  Breakdowns.
  Set Ups and Adjustments.
  Late deliveries (material).
  Operator availability.
Note :
Planned time such as breaks, meetings and maintenance can be considered as losses (useful for encouraging ideas on how to minimise their disruption) as long as a consistent approach is taken.
Notes: <number>
Reasons for classifying breaks, meetings, etc. as losses can be when trying to encourage creative thinking around necessary activities, e.g. staggered break times, more efficient meetings, etc.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 11: Productivity
“The difference between the potential output and actual output, when the equipment was available”
PRODUCTIVITY = IDEAL CYCLE TIME x ACTUAL OUTPUT* x 100%
        AVAILABLE OPERATING TIME
Available operating time
Actual operating
time
Idling / minor
stoppages
3
Speed
4
*Note :- Actual Output is the Quantity of good & bad parts
Notes: <number>
Introduce the equation in basic terms.
1st Animation - Available operating time
After the losses that effect Availability have been accounted for this leaves Available operating time.
2nd Animation - Actual operating time
Further losses occur which effect productivity and leave Actual operating time.
Those key losses include Idling / minor stoppages and Speed.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 12: Operating Speed v Productivity
Operating Speed Rate
  The % of actual cycle time against ideal cycle time.
Productivity
  The Operating Speed Rate factored with interruptions to constant processing, i.e. idling and minor stoppages.
Notes: <number>
Ask for reasons why the operating speed might not be equal to the ideal cycle:-
Hidden machine problems (electrical/mechanical)
The Standard is not known
The Standard has not been communicated
In short, a lack of focus on it
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 13: Quality
“The total good parts produced expressed as a % of the total parts produced”
QUALITY= PARTS MADE – DEFECT QUANTITY x 100%
        PARTS MADE
Actual operating
time
Effective operating time
Defects in process
and rework
5
Start up losses
6
Notes: <number>
Introduce the equation in basic terms.
1st Animation - Actual operating time
After the losses that effect Availability and Productivity have been accounted for this leaves Actual operating time.
2nd Animation - Effective operating time
Further losses occur which effect Quality and leave Effective operating time.
Those key losses include Defects in process and rework and Start up losses
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 14: Processed v Defect Quantity
Parts Made
  The total quantity of parts produced in the available time.
Defect Quantity
  The quantity of parts that did not meet the required standard (including rework) in the available time.
Notes: <number>
The biggest loss to production is often the time required to re-work a component to the required quality standard. This can often be longer than the original process time.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 15: OEE and the Six Big Losses
Equipment
Available time
Available operating time
Actual operating
time
Effective operating time
Six Big Losses
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Notes: <number>
So we’ve seen how the effective operating time for a piece of equipment can be reduced due to ineffective working practices and conditions.
What are the “6 Big Losses”?
These 6 types of losses should give you a start point for the data to be collected and the areas to be targeted as part of the OEE study.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 16: Six Big Losses - What Are They ?
The time lost due to key equipment breaking down or deterioration which causes the production to be stopped for more than 10 min.
Six Big Losses
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Notes: <number>
More than 10 mins from the point the machine stopped adding value to the component to the point which it starts again.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 17: Six Big Losses - What Are They ?
The time lost through “product change over and adjustment ” to the point where the production of the new product is completely satisfactory.
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Six Big Losses
Notes: <number>
The time from the last complete component (operation) to the start of the first new component (operation), under stable conditions, i.e. the equipment must be capable of repeatable performance.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 18: Six Big Losses - What Are They ?
The time lost through key equipment being stopped for less than 10 min.
Time lost during the standard cycle when the equipment is not adding value.
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Six Big Losses
Notes: <number>
Minor stoppages to the process.
Examples :- Change a drill bit
Top up lubrication
Adjust the speeds and feeds
Check the quality
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 19: Six Big Losses - What Are They ?
The time lost through key equipment not producing parts at its optimum rate.
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Six Big Losses
Notes: <number>
It is vital that the standards are known and adhered.
This measure is often able to be generated automatically by the equipment.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 20: Six Big Losses - What Are They ?
The time lost through key equipment not producing parts that meet the specified quality standard.
The time lost through key equipment being utilised to rework sub-standard parts.
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Six Big Losses
Notes: <number>
The biggest loss to production is often the time required to re-work a component to the required quality standard. This can often be longer than the original process time.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 21: Six Big Losses - What Are They ?
The time lost through key equipment not producing parts to the specified quality standard, following start up and before the equipment achieves controllable production conditions.
Breakdowns
1
Setup / adjustment
2
Idling / minor
stoppages
3
Speed
4
Defects in process
and rework
5
Start up losses
6
Six Big Losses
Notes: <number>
It is often the case that equipment, particularly older equipment, will not run to a consistent quality until it has “warmed up sufficiently, i.e. after prolonged stoppages when the hydraulic systems have been “cold” for some time”.
There may also be losses at start up which effect speed and breakdowns, i.e. machines may not get to full operating speed immediately and a high % of breakdowns occur when machines are “cold”.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 22: How to collect data for OEE
Key Points
  OEE is a measure of the equipment or process, not the operators productivity.
  Keep it simple.
  Ensure the process of measuring and applying OEE involves the people who use the equipment.
  Make data collection second nature not a hindrance.
  Understand the process.
  Obtain the data on fixed frequency.
  Snap shot v continuous.
  Units of time (1 min, 10 mins, 30 mins, etc.).
  Automatic or manual data collection.
  Ownership.
  Partnership – those completing sheets and those collecting/collating.
  Regular communication of results.
  Response to trends, peaks and troughs.
Notes: <number>
Stress the need for the team approach and that the people operating pieces of equipment are best placed to identify their problems (using their 5 senses) and potential solutions.
Operators must be involved in how the data will be collected and the counter measures that arise from them.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 23: How to collect data for OEE
Example : Three Hourly Data Sheet
Notes: <number>
Remember that the method for collecting OEE is determined by the equipment you are monitoring, i.e. the level and detail required will be determined by how much is already known of the equipment and how far along the process you are, i.e. start with broad categories of losses and bring in more detail as more is learnt.
Picking a suitable period for measurement and scale of measurement is also key, too much detail can lead to too much wasted time by operators in completing the data sheets, swiftly leading to a lack of belief in the process.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 24
How to collect data for OEE
Notes: <number>
Set up the number crunching in as simple a format as possible, if only a limited number of machines are being monitored, keep the process manual.
If there is a significant level of detail and/or a large number of pieces of equipment being monitored, then a spreadsheet to do the hard work would be recommended.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 25: How to Eliminate Losses ?
Notes: <number>
Many of the common tools within the umbrella of Lean will be important when addressing the losses identified as part of the OEE data collection.
These examples are not the whole picture but together with other methodologies now included within the APS, all the issues identified can be tackled in a systematic manner.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 26: How Do We Use OEE?
OEE is only a measure, its benefits will be lost if the shortfalls it identifies are not acted upon.
OEE is a total measure of performance but the data used to produce it must be used to prioritise improvement tasks.
The purpose of measurement is to identify losses, remove waste and drive improvement.
OEE should be used to support the Total Productive Maintenance (TPM) approach and the tools it supplies.
Notes: <number>
OEE is a measure it will do nothing by itself!
OEE must be used as part of a total approach to equipment effectiveness.
Track the losses and draw a pareto chart to identify the biggest losses.
Problem solve the biggest losses to identify root cause and implement permanent corrective actions.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 27: What are the benefits of OEE?
FOCUS
  Highlight priorities for change.
SIMPLICITY
  Even complex processes can be measured.
FEEDBACK
  Before and after change.
BENCHMARKING
  Objective comparisons.
TARGET SETTING
  Setting achievable goals.
Notes: <number>
In summary, the benefits of using OEE are:-
FOCUS: Identifies what the largest losses are
SIMPLICITY: One measure to express a machines performance
FEEDBACK: How do you judge an improvement unless you can measure it.You must be able to measure before and after.
BENCHMARKING : How do you know how effective your process or equipment is, unless you have an objective measure to compare with other businesses, departments, etc.
TARGET SETTING : You need to be able to set goals and targets in order to measure the effectiveness of the counter measures.
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 28: Solving Problems
OEE
OEE
M/c # 1
LVER 2
M/c # 3
X Hours
X Hours
OEE
Weekly
Production
MRP
Daily
APS Meeting
Support NC OPS Log. Maint. Quality
Customer protection
Counter measure
Equip. uptime
Improve Quality
Improve Performance
2 Weeks
24 Hours
M/c # 2
M/c # 4
OEE
Notes: <number>
Explain the schematic to the delegates in detail.
Emphasise the fact that data is drawn from the machines BY the operator, and fed into an OEE chart, this then gives us valuable information that we can base improvements on. (such as performance, quality and equipment uptime improvements!!!)
This valuable information is also fed into a number of review sessions (such as the APS Meeting review)
Extra Info
Available
Prepared
Flip chart
Photo
Training
Matl.
Flip Chart
Verbal
Slide

## Slide 29
www.BeyondLean.com
Thank You!